## Slide 1: Application of ART neural networks in Wireless sensor networks
Marković Miljan
3139/2011
miljan.markovic@gmail.com

## Slide 2: Problem definition
WSNs operate on large
and often inaccessible areas
Environments they collect data from
are not well defined and dynamic
Prolonging battery life of sensor nodes
is a critical requirement
They typically produce large amounts of raw data
Transfer of such data to a data center
where it would be processed is
highly energy inefficient

## Slide 3: Problem definition
Processing data within the network
must also be adaptable to changes in environment
Organization of WSN:
  Each sensor unit (node) consists of:
    Multiple sensors
    Data processing unit
    A battery
    A radio unit
  Many sensor units form a cluster
  Each cluster has a chosen node (cluster head)
  that collects the data and forwards it to data centers
    Typically has much more resources
    (often continuous power source)
    and is deployed on accessible places

## Slide 4: Problem importance
Without efficient energy consumption,
sensor nodes quickly die out.
It is often very hard to replace them.
It is hard to adapt to changing environments.

## Slide 5: Problem trend
WSNs are important source of information
about the world around us.
  Prediction of natural disasters
  Remote monitoring
  Border line security
With more energy efficient ways of employing single sensor node,
deployment and maintaining of WSNs becomes more plausible and more cost effective
in wider range of environments

## Slide 6: Existing solutions
Data aggregation
Distributed K-means clustering
Classic layered neural network

## Slide 7: Existing solutions (1)
Data aggregation
  Data is sent to selected nodes and aggregated there providing dimensionality reduction
  (+) Simplicity
  (+) Requires little computing power
  (-) Loss of data
  (-) Selecting the same node frequently creates a hotspot
  (-) Depends on efficient routing within WSN
  (-) Not very informative in the end

## Slide 8: Existing solutions (2)
Distributed K-means
  A version of K-means clustering
  that performs it’s operation in peer-to-peer network
  (+) A well defined, proven algorithm
  (+) Outputs a single class ID instead of array of raw values
  (-) Requires a lot of processing
  (-) Excessive node communication
  (-) Requires knowing the number of data clusters in advance

## Slide 9: Existing solutions (3)
Classification using a neural network
  A 3 layer neural network performs classification of data, both on per node basis and on the sensor cluster level.
  (+) Simple to implement
  (+) Outputs a single class ID instead of array of raw values
  (-) Requires a lot of training
  (-) Not adaptable to changes in the environment

## Slide 10: Proposed solution
ART (adaptive resonance theory) is a theory
developed by Stephen Grossberg and Gail Carpenter
The theory describes a number of neural network models
They use supervised and unsupervised learning methods,
and address problems such as
pattern recognition
and prediction

## Slide 11: Proposed solution
Various ART neural networks:
  ART1
    basic model, allowing only binary inputs
  ART2 (A)
    extends network capabilities to support continuous inputs
  Fuzzy ART
    implements fuzzy logic into ART’s pattern recognition,
    thus enhancing generalizability
  ART3
    builds on ART-2 by simulating rudimentary neurotransmitter regulation of synaptic activity
  ARTMAP and fuzzy ARTMAP
    also known as Predictive ART,
    combines two slightly modified ART-1, ART-2 or fuzzyART units
    into a supervised learning structure

## Slide 12: Proposed solution (ART1 organisation)
Input vektor
F1
F2
G1
G2
R
Sloj F2:
Recognition layer
Lateral inhibition
3 groups of inputs
Output vector U
Inhibitory connection to G1
Excitatory connections with weights Wji to F1
Orienting subsystem:
Activated if S is different enough from input vector
Vigilance factor ρ
Aroused with input vector
Inhibited by S vector
Reset signal is sent to all neurons in F2
Attentional subsystem:
Neurons G1 and G2
Coordination between network layers and the rest of the system
Rule 2/3 (2 out of 3)
Aroused by input vector
G1 is inhibited by U
Output signal is sent to all neurons in F1 and F2
Layer F1:
Comparation layer
3 groups of inputs
Output vector S
Inhibitory connection to R
Excitatory connections with Wij weights to F2

## Slide 13: Proposed solution (ART1 activity)
Input vektor
F1
F2
G1
G2
R
Step 1:
Input vector I comes to inputs of F1, R, G1 and G2
Each node in F1 gets one bit
G1 and G2 are activated and send signals to F1 and F2
Activation vector X appears across the nodes of F1
Output vector S appears on outputs of F1
S is exactly equal to I and eliminates it’s effect on R; R remains inactive.
Step 2:
Elements of S are multiplied with Wij and added creating a net input vector T
Elements of T come to inputs of F2
Activation vector Y appears across the nodes of F2
This results in output vector U appearing across nodes of F2
Step 3:
Elements of U are multiplied with Wji and added creating vector V
Elements of V come to inputs of F1, and at the same time element s of U inhibit G1
A new activation vector X* appears across neurons in F1 (X*=IV)
This results in new output vector S*
Step 4 (case 1):
If (│S*│/ │I│<ρ) the network enters a resonant state.
In this state R remains inactive
The weights Wij and Wji are modified.
This way a network learns to recognize a pattern
Step 4 (case 2):
If (S*│/ │I│>ρ), S* no longer can inhibit R
R sends reset signal to F2
Activated neuron in F2 turns off and is excluded from further classification.
Everything repeats from step 1.
If all neurons are exhausted, a network assigns new neuron in F2
This way network learns a new pattern.

## Slide 14: Proposed solution (learning)
Different learning techniques are possible
with ART neural networks.
There are two basic techniques:
  Fast learning
    new values of W are assigned in at discreet moments in time and are determined by algebraic equations
  Slow learning
    values of W at given point in time are determined
    by values of continuous functions at that point
    and described with differential equations.

## Slide 15: Proposed solution (WSN application)
Classification on the cluster level can be organized in various ways depending on the needs.
Following cluster organizations are possible:
  Only one sensor unit in cluster (cluster head) implements ART and other units supply raw data to it.
  Every unit in cluster implements ART
  and data is broadcasted to all units.
  Every unit implements ART but only performs local classification,
  cluster head receives classified data
  and performs cluster level classification on it.

## Slide 16: Conclusion
ART neural networks are surprisingly stable in real world environments, and allow for high accuracy pattern recognition,
even in constantly changing environments
Their nature as neural networks makes them energy efficient.
This makes them very suitable for application in wireless sensor networks