## Slide 1
Ana Naumović Bojana Milašinović ananaumovic@yahoo.com bojanamilasinovic@yahoo.com
School of Electrical Engineering School of Electrical Engineering
University of Belgrade University of Belgrade
Prof. Dr Veljko Milutinović
vm@etf.bg.ac.yu
School of Electrical Engineering
University of Belgrade
PCI Express System Architecture

## Slide 2: Table of Contents
2
PCI vs PCI Express
3
PCI Express Topology
4
PCI Express Overview
5
PCI Express Transactions
6
PCI Express Device Layers
1
Introduction

## Slide 3: Table of Contents
2
PCI vs PCI Express
3
PCI Express Topology
4
PCI Express Overview
5
PCI Express Transactions
6
PCI Express Device Layers
1
Introduction

## Slide 4: Introduction 1
PCI Express is the third-generation Peripheral Component Inter-connect technology for a wide range of systems and peripheral devices.
It is used in mobile, desktop, workstation, server and communication platforms.

## Slide 5: Introduction 2
PCI Express implements a serial, point-to-point, dual simplex type interconnect.
It provides significantly high performance, high speed and reliability bus, compared with predecessor buses.
Currently, transmission and reception data rate is 2.5 Gb/s, but it is expected that frequency to double to 5 Gbits/sec.

## Slide 6: Introduction 3
Multiple PCI Express devices are interconnected via switches, so large number of devices can be connected togehter in a system.
A switch can range from a 2-port device to an n-port device, where each port connects to a PCI Express Link.

## Slide 7: Table of Contents
2
PCI vs PCI Express
3
PCI Express Topology
4
PCI Express Overview
5
PCI Express Transactions
6
PCI Express Device Layers
1
Introduction

## Slide 8: PCI vs PCI Express
“Don't Throw Away What is Good!
Keep It!”

## Slide 9: PCI vs PCI Express What is PCI?
PCI and PCI-X buses are multi-drop, parallel, interconnect buses, in which many devices share one bus.

## Slide 10: PCI vs PCI Express PCI Bus Based System
Graphics Bus System Memory Bus
IO
Devices
Lower performance peripherals

## Slide 11: PCI vs PCI Express Compatibility
PCI Express is software backwards compatible with PCI and PCI-X systems.
It support chip-to-chip interconnect and board-to-board interconnect via cards and connectors, which structure is similar to PCI cards and connectors.

## Slide 12: PCI vs PCI Express Cost
A serial interconnect between two devices results in fewer pins per device package, which means that PCI Express chip and board design cost and board design complexity are reduced.

## Slide 13: Table of Contents
2
PCI vs PCI Express
3
PCI Express Topology
4
PCI Express Overview
5
PCI Express Transactions
6
PCI Express Device Layers
1
Introduction

## Slide 14: PCI Express Topology
The Root Complex is the connection between CPU, memory and PCI Express fabric.
Endpoints are peripheral devices, such as Ethernet, USB
Hierarchy Domain
Hierarchy

## Slide 15: Table of Contents
2
PCI vs PCI Express
3
PCI Express Topology
4
PCI Express Overview
5
PCI Express Transactions
6
PCI Express Device Layers
1
Introduction

## Slide 16: PCI Express Overview Link and Lane
A PCI Express interconnect consists of either x1, x2, x4, x8, x16 or x32 point-to-point Link.
A Lane consists of signal pairs in each direction.
A x1 Link consists of 1 Lane or 1 differential signal pair in each direction.
The Link supports a symmetric number of Lanes in each direction.

## Slide 17: PCI Express Overview Differential Signaling
A positive voltage difference between the D+ and D- terminals implies Logical 1.
A negative voltage difference between D+ and D- implies a Logical 0.
No voltage difference between D+ and D- means
that the driver is in the high-impedance tristate condition.

## Slide 18: PCI Express Overview Packet Based Protocol
Packets are transmitted and received serially and byte striped across the available Lanes of the Link.
The more Lanes implemented on a Link the faster a packet is transmitted and the greater the bandwidth of the Link.

## Slide 19: PCI Express Overview Quality of Service, Traffic Class and Virtual Channels
The Quality of Service (QoS) feature of PCI Express refers to the capability of routing packets from different applications through the fabric with differentiated priorities.
PCI Express packets contain a Traffic Class (TC) number between 0 and 7.
These packets are routed through the fabric by utilizing virtual channel (VC) buffers.
Each Traffic Class is individually mapped to a Virtual Channel.

## Slide 20: PCI Express Overview Flow Control
A packet transmitted by a device is received into a VC buffer in the receiver at the opposite end of the Link.
The protocol by which the transmitter ensures that the receiving buffer has sufficient space available is referred to as flow control.
The receiver periodically updates the transmitter with information regarding the amount of buffer space it has available.

## Slide 21: Table of Contents
2
PCI vs PCI Express
3
PCI Express Topoplogy
4
PCI Express Overview
5
PCI Express Transactions
6
PCI Express Device Layers
1
Introduction

## Slide 22: PCI Express Transactions
Transmission and reception of packets
Transaction Layer Packets
Four categories:
memory
IO
configuration
message

## Slide 23: TLP Packet Types
non posted
posted
memory read (MRd)
IO read (IORd)
IO write (IOWr)
configuration read (CfgRd)
configuration write (CfgWr)
memory write (MWr)
message (Msg, MsgD)

## Slide 24: Non Posted Transactions
read transaction
- data is in the
completion TLP
root complex or endpoint device
root complex, switches, bridges or endpoint device

## Slide 25
write transaction
- data is in the reception TLP
Non Posted Transactions

## Slide 26: Posted Memory Write Transactions
- data is in the
request TLP
- error handling
software
NO NOTIFICATION!

## Slide 27: Posted Message Transactions
Routing is based on message’s address, device ID or routed implicitly

## Slide 28: Table of Contents
2
PCI vs PCI Express
3
PCI Express Topoplogy
4
PCI Express Overview
5
PCI Express Transactions
6
PCI Express Device Layers
1
Introduction

## Slide 29: PCI Express Device Layers
Transmit portion
Receive portion

## Slide 30: Layers Key Functions
root complex core logic or endpoint core logic
Ethernet controller,
USB controller

## Slide 31: Transaction Layer Packet (TLP)
originates
terminates

## Slide 32: Transaction Layer
the transmit portion
the receive portion
3 DW or 4 DW
contains address, TLP type, transfer size, requester ID/completer ID, tag, …
generated by this layer

## Slide 33: Data Link Layer
the transmit portion
the receive portion
generated and appended
preserves a copy of TLP

## Slide 34: Physical Layer
two portions:
Logical and Electrical Physical Layer
processing packets before transmission on the Link
analog interface of the PL that connects to the Link

## Slide 35: Transaction Layer Packet (TLP)
through the Link
ENCODE?

## Slide 36
Thank you for your attention!