## Slide 1: PCI Express System Architecture
Ana Naumović Bojana Milašinović
ananaumovic@yahoo.com bojanamilasinovic@yahoo.com
Prof. Dr. Veljko Milutinović
vm@etf.bg.ac.yu

## Slide 2: Introduction
5 PCI Bus slots

## Slide 3: Introduction
eripheral
omponent
nterconnect
P
C
P
C
I

## Slide 4
Something You should know about PCI, before we start with PCI Express

## Slide 5: PCI
PCI and PCI-X buses are multi-drop parallel interconnect buses in which many devices share one bus.

## Slide 6: …on the other hand
PCI Express implements a serial, point-to-point type interconnect for communication between two devices.

## Slide 7: PCI Definition
“A personal computer local bus, which runs (usually) at 33 MHz. It provides a high-speed connection with peripherals and allows connection of several peripheral devices. It is an interconnect system for sending data between the CPU and peripherals independently of the processor. The standard allows for 32-bit transmission of up to 132Mb per second, and has found a use in such high data rate applications as digital audio and video. 64-bit PCI busses are also now available”.

## Slide 8: PCI (Overview)
Comparison of Bus Frequency, Bandwidth and Number of Slots
[*] Double all these bandwidth numbers for 64-bit bus implementations

## Slide 9: 33 MHz PCI Bus Based System
Graphics Bus System Memory Bus
IO
devices
Lower performance peripherals
Provides the source of reset, reference clock and error reporting signals

## Slide 10: PCI Bus Cycle
4 GB memory address space
33 MHz
Supports 12 transactions
Handshake signals
32b
(optionally supports 64b)
Address and Data Bus are multiplexed => reduced pin count!

## Slide 11: Electrical Load Limit
PCI bus can support a maximum of 10-12 electrical loads (devices) at 33 MHz.
To connect any more than 10-12 loads in a system requires the implementation of a PCI-to-PCI bridge as shown in Figure

## Slide 12: Transaction Model
Programmed IO transaction
DMA Transaction Model
Peer-to-Peer Transaction
Model
50% efficiency
PCI Device becomes a bus master
Between two PCI devices

## Slide 13: PCI Bus Arbitration
Hidden Bus Arbitration.
It allows for more efficient hand over of the bus from one bus master device to another with only one idle clock between two bus cycles.
Arbitration Algorithm

## Slide 14: Retry Protocol
I step – Initiate
II step – Target
device not
ready
III step – Retry
STOP# (signal retry)

## Slide 15: Disconnect Protocol
I step – Initiate
II step – Some data
transfered
III step – Disconnect
STOP# (signal disconnect)

## Slide 16: Retry / Disconnect
vs.
Retry Disconnect

## Slide 17: PCI Interrupt Handling
INTA#
INTB#
INTC#
INTD#
Allows multiple devices to generate their interrupts on the same interrupt signal

## Slide 18: PCI Error Handling
Notification of a parity error and
a system shuts down
Usually sets NMI signal

## Slide 19: Address Space Mapping
16MB = 256B * 8 func/dev * 32 dev/bus *256 bus/sys

## Slide 20: PCI Configuration Cycle Generation
  Address Port CF8h
  ( IO read )
  Data Port CFCh
  ( IO read/write )
Select the device whose register is being accessed

## Slide 21: Programming Model
The CPU communicates with any PCI device via the North bridge, which generates PCI memory or IO bus cycles on the behalf of the CPU.
An intelligent PCI device that includes a local processor or bus master state machine (typically intelligent IO cards) can also initiate PCI memory or IO transactions on the PCI bus. These masters can communicate directly with any other devices, including system memory associated with the North bridge.

## Slide 22: Latest Generation of PCI Chipsets
Include South Bridge. Doesn’t support ISA bus
The IDE, USB, Ethernet and audio devices do not transfer their data through the
PCI bus to memory as is the case with earlier chipsets.
Instead they do so through the Hub Link.

## Slide 23: 66 MHz PCI Bus Based System
The PCI clock period at 66MHz is 15ns
These buses each support 1 connector in which a high-end peripheral card may be installed.

## Slide 24: PCI vs. PCI Express
“Don't Throw Away What is Good!
Keep It!”

## Slide 25
And now, lets start with PCI Express...

## Slide 26: PCI Express Definition
“PCI Express is the third generation high performance I/O bus used to interconnect peripheral devices in applications such as computing and communication platforms. The first generation buses include the ISA, EISA, VESA, and Micro Channel buses, while the second generation buses include PCI, AGP, and PCI-X. PCI Express is an all encompassing I/O device interconnect bus that has applications in the mobile, desktop, workstation, server, embedded computing and communication platforms .”

## Slide 27: Introduction
Communication involves the transmission and reception of packets called Transaction Layer Packets (TLPs).
PCI Express Transaction
Memory IO Configuration Message Transaction
PCI, PCI-X only PCI Express

## Slide 28: Introduction
Transactions are defined as a series of one or more packet transmissions required to complete an information transfer between a requester and a completer.

## Slide 29: Non-Posted Read Transactions
The completion packet contains routing information necessary to route the packet back to the requester. This completion packet travels through the same path and hierarchy of switches as the request packet.
can be a root complex, switches, bridges or endpoints
may be root complex or endpoint devices

## Slide 30: Non-Posted Write Transactions
The completer creates a single completion packet without data (Cpl) to confirm reception of the write request.
may be root complex or endpoint devices
can be a root complex, switches, bridges or endpoints

## Slide 31: Posted Memory Write Transactions
If the write request is received
by the completer in error, or
is unable to write the posted
write data to the final destination
due to an internal error, the requester
is not informed via the hardware
protocol.
Error handling software manages
the error.
The completer returns no completion notification to inform the requester that the memory write request packet has reached its destination successfully.

## Slide 32: Posted Message Transactions
Message transactions are used for PCI style legacy interrupt signaling, power management protocol, error signaling, unlocking a path in the PCI Express fabric, slot power support, hot plug protocol, and vender defined purposes.

## Slide 33: PCI Express Device Layers Overview
Packet contents are formed in this layer.
This packet is referred to as a Transaction Layer Packet (TLP).
Concatenates to the packet additional information required for error checking.
Encode the packet and transmit differentially on the Link by the analog portion of this Layer.
Decodes the incoming packet contents and forwards the resulting contents to the upper layers.
Checks for errors in the incoming packet and if there are no errors forwards the packet up to the Transaction Layer.
Buffers the incoming TLPs and converts the information in the packet to a representation that can be processed by the device core and application.

## Slide 34: Device Layers and their Associated Packets
Transaction Layer Packet (TLP)
Data Link Layer Packet (DLLP)
Physical Layer Packet (PLP)

## Slide 35: Transaction Layer Packets (TLPs)
The ECRC field is used by the ultimate targeted device of this packet to check for CRC errors in the header and data portion of the TLP.
The LCRC field is used by the neighboring receiver device at the other end of the Link to check for CRC errors in the core section of the TLP plus the sequence ID.
The Header is 3 doublewords or 4 doublewords in size and may include information such as; Address, TLP type, transfer size, requester ID/completer ID, tag, traffic class, byte enables, completion codes, and attributes.

## Slide 36: Data Link Layer Packets (DLLPs)

## Slide 37: Physical Layer Packets (PLPs)
PLPs are used to place a Link into the electrical idle low power state or to wake up a link from this low power state.
1 Byte 3 or more characters

## Slide 38: Function of Each PCI Express Device Layer
Consists of, for example, the root complex core logic or an endpoint core logic such as that of an Ethernet controller, SCSI controller, USB controller, etc.
The transaction layer contains virtual channel buffers (VC Buffers) to store outbound TLPs that await transmission and also to store inbound TLPs received from the Link.

## Slide 39: Device Core / Software Layer (1)
The Device Core consists of, for example, the root complex core logic or an endpoint core logic such as that of an Ethernet controller, USB controller, etc.
To design a PCI Express endpoint, a designer may reuse the Device Core logic from a PCI or PCI-X core logic design and wrap around it the PCI Express layered design described in this section.

## Slide 40: Device Core / Software Layer (2)
Transmit Side
The Device Core logic in conjunction with local software provides the necessary information required by the PCI Express device to generate TLPs. This information is sent via the Transmit interface to the Transaction Layer of the device. Example of information transmitted to the Transaction Layer includes: transaction type to inform the Transaction Layer what type of TLP to generate, address, amount of data to transfer, data, traffic class, message index etc.

## Slide 41: Device Core / Software Layer (3)
Receive Side
The Device Core logic is also responsible to receive information sent by the Transaction Layer via the Receive interface. This information includes: type of TLP received by the Transaction Layer, address, amount of data received, data, traffic class of received TLP, message index, error conditions etc.

## Slide 42: Transaction Layer (1)
The transaction Layer is responsible for generation of outbound TLP traffic and reception of inbound TLP traffic. The Transaction Layer supports the split transaction protocol for non-posted transactions. In other words, the Transaction Layer associates an inbound completion TLP of a given tag value with an outbound non-posted request TLP of the same tag value transmitted earlier.

## Slide 43: Transaction Layer (2)
The transaction layer contains virtual channel buffers (VC Buffers) to store outbound TLPs that await transmission and also to store inbound TLPs received from the Link
The Transaction Layer also orders TLPs according to ordering rules before transmission.
This layer supports the Quality of Service (QoS) protocol.
The Transaction Layer supports 4 address spaces: memory address, IO address, configuration address and message space.

## Slide 44: Transaction Layer Transmit Side (1)
The Transaction Layer receives information from the Device Core and generates outbound request and completion TLPs which it stores in virtual channel buffers. This layer assembles Transaction Layer Packets (TLPs).

## Slide 45: Transaction Layer Transmit Side (2)
The Transaction Layer receives information from the Device Core and generates outbound request and completion TLPs which it stores in virtual channel buffers. This layer assembles Transaction Layer Packets (TLPs).

## Slide 46: Transaction Layer Receiver Side (1)
The receiver side of the Transaction Layer stores inbound TLPs in receiver virtual channel buffers. The receiver checks for CRC errors based on the ECRC field in the TLP. If there are no errors, the ECRC field is stripped and the resultant information in the TLP header as well as the data payload is sent to the Device Core.

## Slide 47: Transaction Layer Flow Control
The Transaction Layer ensures that it does not transmit a TLP over the Link to a remote receiver device unless the receiver device has virtual channel buffer space to accept TLPs.
The protocol for guaranteeing this mechanism is referred to as the "flow control" protocol.
If the transmitter device does not observe this protocol, a transmitted TLP will cause the receiver virtual channel buffer to overflow.

## Slide 48: Transaction Layer Quality of Service (QoS)
QoS refers to the capability of routing packets from different applications through the fabric with differentiated priorities and deterministic latencies and bandwidth. PCI and PCI-X systems do not support QoS capability.

## Slide 49: Transaction Layer Traffic Classes (TCs) and Virtual Channels (VCs)
TC is a TLP header field transmitted within the packet unmodified end-to-end through the fabric.
VCs are physical buffers that provide a means to support multiple independent logical data flows over the physical Link via the use of transmit and receiver virtual channel buffers.

## Slide 50: Transaction Layer Traffic Classes (TCs) and Virtual Channels (VCs)
PCI Express devices may implement up to 8 VC buffers (VC0-VC7).
The TC field is a 3-bit field that allows differentiation of traffic into 8 traffic classes (TC0-TC7).
Devices must implement VC0.
A device is required to support TC0
(best effort general purpose service class).

## Slide 51: Transaction Layer Traffic Classes (TCs) and Virtual Channels (VCs)

## Slide 52: Transaction Layer Port Arbitration and VC Arbitration
The goals of arbitration support in the Transaction Layer are:
- To provide differentiated services between data flows within the fabric.
- To provide guaranteed bandwidth with deterministic and smallest end-to-end transaction latency.

## Slide 53: Transaction Layer Port Arbitration and VC Arbitration
Independent of arbitration, each VC must observe transaction ordering and flow control rules before it can make pending TLP traffic visible to the arbitration mechanism.
Endpoint devices and a root complex with only one port do not support port arbitration. They only support VC arbitration in the Transaction Layer.

## Slide 54: Transaction Layer Port Arbitration and VC Arbitration
Switches implement two types of arbitration for each egress port: Port Arbitration and VC Arbitration

## Slide 55: Transaction Layer Port Arbitration
Port arbitration is arbitration between two packets arriving on different ingress ports but that map to the same virtual channel (after going through TC-to-VC mapping) of the common egress port.
The port arbiter implements round-robin, weighted round-robin or programmable time-based round-robin arbitration schemes selectable through configuration registers.

## Slide 56: Transaction Layer VC Arbitration
VC arbitration takes place after port arbitration. For a given egress port, packets from all VCs compete to transmit on the same egress port.
VC arbitration resolves the order in which TLPs in different VC buffers are forwarded on to the Link.
VC arbitration policies supported include, strict priority, round-robin and weighted round-robin arbitration schemes selectable through configuration registers.

## Slide 57: Transaction Layer
Includes :
- Transaction Ordering protocol implements PCI/PCI-X compliant producer-consumer ordering model for transaction ordering with provision to support relaxed ordering similar to PCI-X architecture.
- Power Management
- Configuration Registers- configured during initialization and bus enumeration. They are also configured by device drivers and accessed by runtime software/OS.

## Slide 58: Data Link Layer
The primary function of the Data Link Layer is to ensure data integrity during packet transmission and reception on each Link.
With error checking and automatic replay of packets received in error, PCI Express ensures very high probability that a TLP transmitted by one device will make its way to the final destination with no errors. This makes PCI Express ideal for low error rate, high-availability systems such as servers.

## Slide 59: Data Link Layer Transmit side
The Data Link Layer is responsible for TLP CRC generation and TLP error checking.

## Slide 60: Data Link Layer Receive side
The receive side of the Data Link Layer is responsible for LCRC error checking on inbound TLPs. If no error is detected, the device schedules an ACK DLLP for transmission back to the remote transmitter device. The receiver strips the TLP of the LCRC field and sequence ID.
If a CRC error is detected, it schedules a NAK to return back to the remote transmitter. The TLP is eliminated.
The receive side of the Data Link Layer also receives ACKs and NAKs from a remote device.
The receive side is also responsible for checking the sequence ID of received TLPs to check for dropped or out-of-order TLPs.

## Slide 61: Data Link Layer Contribution to TLPs and DLLPs
The Data Link Layer concatenates a 12-bit sequence ID and 32-bit LCRC field to an outbound TLP that arrives from the Transaction Layer.
The sequence ID is used to associate a copy of the outbound TLP stored in the replay buffer with a received ACK/NAK DLLP inbound from a neighboring remote device. The ACK/NAK DLLP confirms arrival of the outbound TLP in the remote device.

## Slide 62: EXAMPLES

## Slide 63: Non-Posted Transaction Showing ACK-NAK Protocol
  Step 1a. Requester transmits a memory read request TLP (MRd). Switch receives the MRd TLP and checks for CRC error using the LCRC field in the MRd TLP.
  Step 1b. If no error then switch returns ACK DLLP to requester. Requester discards copy of the TLP from its replay buffer.

## Slide 64: Non-Posted Transaction Showing ACK-NAK Protocol
  Step 2a. Switch forwards the MRd TLP to the correct egress port using memory address for routing. Completer receives MRd TLP. Completer checks for CRC errors in received MRd TLP using LCRC.
  Step 2b. If no error then completer returns ACK DLLP to switch. Switch discards copy of the MRd TLP from its replay buffer.

## Slide 65: Non-Posted Transaction Showing ACK-NAK Protocol
  Step 3a. Completer checks for CRC error using optional ECRC field in MRd TLP. Assume no End-to-End error. Completer returns Completion (CplD) with Data TLP whenever it has the requested data. Switch receives CplD TLP and checks for CRC error using LCRC.
  Step 3b. If no error then switch returns ACK DLLP to completer. Completer discards copy of the CplD TLP from its replay buffer.

## Slide 66: Non-Posted Transaction Showing ACK-NAK Protocol
  Step 4a. Switch decodes Requester ID field in CplD TLP and routes the packet to the correct egress port. Requester receives CplD TLP. Requester checks for CRC errors in received CplD TLP using LCRC.
  Step 4b. If no error then requester returns ACK DLLP to switch. Switch discards copy of the CplD TLP from its replay buffer. Requester determines if there is error in CplD TLP using CRC field in optional ECRC field. Assume no End-to-End error. Requester checks completion error code in CplD. Assume completion code of 'Successful Completion'. To associate the completion with the original request, requester matches tag in CplD with original tag of MRd request. Requester accepts data.

## Slide 67: Non-Posted Transaction on Link

## Slide 68: Posted Transaction Showing ACK-NAK Protocol
  Step 1a. Requester transmits a memory write request TLP (MWr) with data. Switch receives MWr TLP and checks for CRC error with LCRC field in the TLP.
  Step 1b. If no error then switch returns ACK DLLP to requester. Requester discards copy of the TLP from its replay buffer.

## Slide 69: Posted Transaction Showing ACK-NAK Protocol
  Step 2a. Switch forwards the MWr TLP to the correct egress port using memory address for routing. Completer receives MWr TLP. Completer checks for CRC errors in received MRd TLP using LCRC.
  Step 2b. If no error then completer returns ACK DLLP to switch. Switch discards copy of the MWr TLP from its replay buffer. Completer checks for CRC error using optional digest field in MWr TLP. Assume no End-to-End error. Completer accepts data. There is no completion associated with this transaction.

## Slide 70: Posted Transaction on Link

## Slide 71: Physical Layer
The Physical Layer is divided in two portions, the Logical Physical Layer and the Electrical Physical Layer.
The Logical Physical Layer contains digital logic associated with processing packets before transmission on the Link, or processing packets inbound from the Link before sending to the Data Link Layer.
The Electrical Physical Layer is the analog interface of the Physical Layer that connects to the Link. It consists of differential drivers and receivers for each Lane.

## Slide 72: Physical Layer Transmit Side
TLPs and DLLPs from the Data Link Layer are clocked into a buffer in the Logical Physical Layer. The Physical Layer frames the TLP or DLLP with a Start and End character. The symbol is a framing code byte which a receiver device uses to detect the start and end of a packet.

## Slide 73: Physical Layer Transmit Side
The resultant bytes are encoded into a 10b code by the 8b/10b encoding logic. The primary purpose of encoding 8b characters to 10b symbols is to create sufficient 1-to-0 and 0-to-1 transition density in the bit stream to facilitate recreation of a receive clock with the aid of a PLL at the remote receiver device.
The parallel-to-serial converter generates a serial bit stream of the packet on each Lane and transmits it differentially at 2.5 Gbits/s.

## Slide 74: Physical Layer Receive Side
The receive Electrical Physical Layer clocks in a packet arriving differentially on all Lanes. The serial bit stream of the packet is converted into a 10b parallel stream using the serial-to-parallel converter. The receiver logic also includes an elastic buffer which accommodates for clock frequency variation between a transmit clock with which the packet bit stream is clocked into a receiver and the receiver clock. The 10b symbol stream is decoded back to the 8b representation of each symbol with the 8b/10b decoder. The 8b characters are de-scrambled. The Byte unstriping logic, re-creates the original packet stream transmitted by the remote device.

## Slide 75: Link Training and Initialization
An additional function of the Physical Layer is Link initialization and training.
Link initialization and training is a Physical Layer controlled process that configures and initializes each Link for normal operation.
This process is automatic and does not involve software.

## Slide 76: Link Training and Initialization
The following are determined during the Link initialization and training process:
Link width
Link data rate
Lane reversal
Polarity inversion.
Bit lock per Lane
Symbol lock per Lane
Lane-to-Lane de-skew within a multi-Lane Link.

## Slide 77: EXPLANATIONS

## Slide 78: Link width
Two devices with a different number of Lanes per Link may be connected. E.g. one device has x2 port and it is connected to a device with x4 port. After initialization the Physical Layer of both devices determines and sets the Link width to the minimum Lane width of x2. Other Link negotiated behaviors include Lane reversal and splitting of ports into multiple Links.

## Slide 79: Lane reversal
Lane reversal if necessary is an optional feature. Lanes are numbered. A designer may not wire the correct Lanes of two ports correctly. In which case training allows for the Lane numbers to be reversed so that the Lane numbers of adjacent ports on each end of the Link match up. Part of the same process may allow for a multi-Lane Link to be split into multiple Links.

## Slide 80: Polarity inversion
The D+ and D- differential pair terminals for two devices may not be connected correctly. In which case the training sequence receiver reverses the polarity on the differential receiver.

## Slide 81: Link data rate
Training is completed at data rate of 2.5 Gbit/s. In the future, higher data rates of 5 Gbit/s and 10 Gbit/s will be supported. During training, each node advertises its highest data rate capability. The Link is initialized with the highest common frequency that devices at opposite ends of a Link support.

## Slide 82: Lane-to-Lane De-skew
Due to Link wire length variations and different driver/receiver characteristics on a multi-Lane Link, bit streams on each Lane will arrive at a receiver skewed with respect to other Lanes. The receiver circuit must compensate for this skew by adding/removing delays on each Lane. Relaxed routing rules allow Link wire lengths in the order of 20"-30".

## Slide 83: Reset
Two types of reset are supported:
- Cold/warm reset also called a Fundamental Reset which occurs following a device being powered-on (cold reset) or due to a reset without circulating power (warm reset).
- Hot reset sometimes referred to as protocol reset is an in-band method of propagating reset. Transmission of an ordered-set is used to signal a hot reset. Software initiates hot reset generation.

## Slide 84: Electrical Physical Layer
The transmitter of one device is AC coupled to the receiver of another device at the opposite end of the Link.

## Slide 85: Hot Plug
PCI Express supports native hot-plug though hot-plug support in a device is not mandatory. Some of the elements found in a PCI Express hot plug system are:
Indicators which show the power and attention state of the slot.
Manually-operated Retention Latch (MRL) that holds add-in cards in place.
MRL Sensor that allow the port and system software to detect the MRL being opened.
Electromechanical Interlock which prevents removal of add-in cards while slot is powered.
Attention Button that allows user to request hot-plug operations.
Software User Interface that allows user to request hot-plug operations.
Slot Numbering for visual identification of slots.

## Slide 86: PCI Express Performance and Data Transfer Efficiency
DLLPs are 2 doublewords in size. The ACK/NAK and flow control protocol utilize DLLPs, but it is not expected that these DLLPs will use up a significant portion of the bandwidth.
The remainder of the bandwidth is available for TLPs. Between 6-7 doublewords of the TLP is overhead associated with Start and End framing symbols, sequence ID, TLP header, ECRC and LCRC fields.
The remainder of the TLP contains between 0-1024 doublewords of data payload.

## Slide 87: PCI Express Performance and Data Transfer Efficiency
It is apparent that the bus efficiency is significantly low if small size packets are transmitted. The efficiency numbers are very high if TLPs contain significant amounts of data payload.
Packets can be transmitted back-to-back without the Link going idle. Thus the Link can be 100% utilized.

## Slide 88
THANK YOU