## Slide 1: Dataflow Computing
Milos Kotlar
School of Electrical Engineering, University of Belgrade
kotlar.milos@gmail.com

## Slide 2: Big data
The big data applications are taking effort to break the zetta-scale barrier (1021)
The main challenge is finding a way to process such big quantities of data
The ratio of data volume increase is higher than the ratio of processing power increase

## Slide 3: Power dissipation
Most of the existing approaches are dissipating enormous amount of electrical power, by solving big data problems
Conventional microprocessor technology based on the control-flow paradigm has been increasing the clock rate aligned with the Moore's Law, and thus, the processing power has been improved

## Slide 4: Moore’s Law
The silicon technology hit a wall, since power dissipation of silicon technology reached its technological limits
According to Moore’s Law, the standard microprocessor technology has hit the wall

## Slide 5: 40 years of microprocessor trend data

## Slide 6: High-performance computing
The end of Moore's Law leads to the several approaches for solving this problem
The development of high-performance computing systems utilizes other alternative architectural principles, such as the dataflow paradigm

## Slide 7: The dataflow paradigm
The dataflow paradigm introduces computing in space where computations are placed dimensionally on a chip
Such an approach perfectly fits when execution time is not a prime concern, to save space and energy, and with limited space and/or power resources
For big data algorithms, the dataflow paradigm can achieve acceleration consuming much less electrical power

## Slide 8: Conditions for the dataflow paradigm
Over 95% of the algorithm run-time has to be in loops
Acceleration depends on level of data reusability inside the loops
Suitable for data streaming
Latency before the first result is computed
Presents a new programming model
Requires programming effort to accelerate an algorithm

## Slide 9: Maxeler dataflow architecture

## Slide 10: Controlflow vs. dataflow
Controlfow:
  Computing in time
  Number of transistors: ~ 1B (1,000,000,000)
  Clock rate: ~4GHz
Dataflow:
  Computing in space
  Number of transistors: ~ 100M (100,000,000)
  Clock rate: ~200MHz

## Slide 11: Maxeler WebIDE
Programming environment
Simulation

## Slide 12: Exercise 1 - Hello World
Write a Kernel that takes a single input stream x and applies a simple function:

## Slide 13: Application
CPU code
Kernel is a graph of pipelined arithmetic units
Manager describes the data flow choreography between Kernels, the DFE’s memory and the CPU
SLiC Skin enables communication between CPU and DFE
MaxCompiler uses an extended version of Java called MaxJ
Files have the .maxj file extension

## Slide 14: Kernel

## Slide 15: Manager
The Standard Manager provided with MaxCompiler is a general-purpose Manager which supports:
  a single Kernel
  external LMem interfaces
  linking between multiple dataflow engines
  links to the CPU

## Slide 16: Hello World – Kernel code

## Slide 17: Hello World – Manager code

## Slide 18: Hello World – CPU code

## Slide 19: Debugging
simPrintf allow to print values explicitly from streams within the Kernel on every tick
simPrintf behave similarly to printf in C
To print the message only when a certain condition is met, a Boolean DFEVar stream can be supplied as a condition:
  void debug.simPrintf(DFEVar condition, String message, Object... args)
The arguments args can contain Java variables or DFEVar streams.

## Slide 20: Exercise 1
Write a Kernel that takes two single input streams x and y and produces a new output single stream as a summation of the two input streams.
DFEVar io.input(String name, DFEType type)
DFEVar io.output(String name, DFEVar result, DFEType type)

## Slide 21: Software and hardware variables
Software variables exist during the compilation time
Hardware variables exist during the execution time

## Slide 22: Hardware variables
A floating-point type parameterized with mantissa and exponent bit-widths:
  dfeFloat(int exponent_bits, int mantissa_bits)
A fixed-point type with parameterizable size and binary point offset:
  dfeFixOffset(int num_bits, int offset, SignMode sign_mode*)
*SignMode.UNSIGNED ,SignMode.TWOSCOMPLEMENT

## Slide 23: Floating-point vs fixed-point

## Slide 24: Hardware variables
dfeUInt(int bits)
dfeInt(int bits)
dfeBool()
DFERawBits streams are used to prevent invalid operations:
  dfeRawBits()
DFEComplex/DFEVector variables allow multiple variables to be grouped together

## Slide 25
Resource allocation

## Slide 26: Available dataflow operators

## Slide 27: Exercise 2
Write a Kernel that takes two vector input streams x and y and produces a new output vector stream as a summation of the two input streams.
DFEVectorType<DFEVar> vectorType = new DFEVectorType<DFEVar>(DFEType type, int size);

## Slide 28: Exercise 3
Design a Kernel that takes an input vector of four 32-bit unsigned integers, reverses the order of the elements in the vector and sends them back out again.
DFEVectorType<DFEVar> vectorType = new DFEVectorType<DFEVar>(DFEType type, int size);

## Slide 29: Scalar values
Transfer single values to and from the DFE at runtime
  io.scalarInput(name, dfe_type)
In contrast to a parameter passed to the constructor of the Kernel class, which requires recompilation, a scalar input can be set by the CPU application dynamically at runtime

## Slide 30: Exercise 4
Design a Kernel that takes an input vector of 32-bit unsigned integers, reverses the order of the elements in the vector and sends them back out again, using a scalar input for vector size.
DFEVar var = io.scalarInput(name, dfe_type);

## Slide 31: Streams of data
A core concept of dataflow computing is operating on windows into data streams
The data window is held in on-chip memory on the dataflow engine, minimizing off-chip data transfers
Stream offsetting allows us to access data elements within a stream relative to the current location

## Slide 32: Streams of data

## Slide 33: Streams of data

## Slide 34: Streams of data
Maxeler supports three types of stream offsets:
  static offsets have a size fixed at compile-time
    stream.offset(DFEVar in_stream, int constant)
  variable offsets have size set at run time before a stream is processed
    stream.offset(DFEVar in_stream, int constant)
  dynamic offsets have sizes set at run time during stream processing
    stream.offset(KernelObject src, DFEVar offset, int min offset , int max offset)

## Slide 35: Characteristics stream offsets

## Slide 36: Exercise 5
Write a Kernel that computes a 3-point moving average over a sequence of N data values. The moving average can be expressed as:
stream.offset(DFEVar in_stream, int constant)

## Slide 37: Counters
Equivalents of loops in sequential programs
Counters allow Kernel designs to keep track of where they are in the stream and keep track of various levels of streaming and iteration
DFEVar control.count.simpleCounter(int bit_width)

## Slide 38: Advanced counters
Count.Params control.count.makeParams(int bit_width)
Counter control.count.makeCounter(Count.Params params)
Options:
  bit width
  initial value
  increment
  count mode (NUMERIC INCREMENTING, SHIFT LEFT, SHIFT RIGHT)
  maximum value
  wrap mode
  wrap value
  enable

## Slide 39: Exercise 6
Write a Kernel that computes a 3-point moving average over a sequence of N data values. At the boundaries (the beginning and the end of the data sequence), 2-point averages need to be applied.

## Slide 40: Controlled inputs and outputs
Dataflow inputs and outputs could be controlled using streams of Boolean values, telling the gate to be open or closed during each tick
io. input(String name, KernelType type, DFEVar control)
io.output(String name, KernelObject output, KernelType type, DFEVar control)

## Slide 41: DFE memory
Kernel memories are implemented using a special on-chip memory resource.
The number of on-chip BRAM resources required for a particular kernel memory depends on:
The number of items in the memory
The type of the data held in the memory

## Slide 42: DFE memory
DFEs provide two basic kinds of memory:
  FMem (Fast Memory)
  LMem (Large Memory)
On-chip static SRAM which can hold several MBs of data
Off-chip DRAM technology and can hold many GBs of data
All inputs and outputs to kernel memories are streams:
  Streams of addresses go in
  Streams of data come out
  Where data is being written, streams of data input go into the RAM

## Slide 43: On-chip memory
The method alloc returns a Memory object, which can then be used to access the memory:
  Memory<DFEVar> mem.alloc(DFEType type, int depth)
Data can be written into a RAM via the call:
  Memory.write(DFEVar address, DFEVar data, DFEVar enable)
Reading memory from specified addresses:
  Memory.read(DFEVar address)

## Slide 44: Read-write memory
If you write to a memory address in a kernel tick you can not call read with the same address in the same tick.
Attempting to do so will return undefined data.
As an optimization, it is also possible to create a single memory port which both reads and writes in the same tick using the same address:
  DFEVar Memory.port(DFEVar address, DFEVar data in, DFEVar enable, RamWriteMode portMode)

## Slide 45: Mapped ROM memory
Memories can optionally be mapped, which allows them to be changed by the CPU at runtime
For values that change slowly but sufficiently frequently that it would be undesirable to recompile the .max file.
Example:
  Memory<DFEVar> mappedRom = mem.alloc(dfeFloat(8,24), dataSize);
  mappedRom.mapToCPU(”mappedRom”)

## Slide 46: Off-chip memory
Allows large amounts of data to be kept local to the dataflow engine

## Slide 47: Loops in the dataflow engine
In a dataflow implementation, the data is streamed into the Kernel from the Manager, so there is no need for a loop in the Kernel itself: the loop is implicit in the stream.
The Manager controls the streaming of the data from its source, which can be from the CPU directly, from the LMem on the DFE or via MaxRing from another DFE.

## Slide 48: Nested & while loops in the dataflow engine
Counter chain
While loops?

## Slide 49: Cyclic dataflow graph
A cycle in the dataflow graph arises from a dependence from one iteration to the next

## Slide 50: Cyclic dataflow graph

## Slide 51: Autoloop offset
An Autoloop offset is a feature of MaxCompiler that automatically calculates the lowest valid offset for a cycle in the graph
  Stream.OffsetExpr makeOffsetAutoLoop(String name)
  Stream.OffsetExpr makeOffsetAutoLoop(String name, int min size, int max size)
  DFEVar Stream.OffsetExpr.getDFEVar(KernelLib design)

## Slide 52: Autoloop offset

## Slide 53: Multi-tick implementation of the row-sum

## Slide 54: Data dependency

## Slide 55: Multi-tick implementation of the column-sum

## Slide 56: Homework assignments
For each homework assignment, you should take one algorithm from the following sources:
Homework Assignment 1 (Math): http://www.grad.hr/nastava/gs/prg/NumericalRecipesinC.pdf
without (Search, Sorting, Random Numbers, Less-Numerical Algorithms)
Homework Assignment 2 (Image Understanding): http://homepages.inf.ed.ac.uk/rbf/BOOKS/PHILLIPS/cips2ed.pdf
Homework Assignment 3 (Machine Learning): http://stanford.edu/~rezab/nips2014workshop/

## Slide 57: Math examples
Homework assignment 1

## Slide 58: Linear correlation
Given a set of observations (x1, y1), (x2,y2),...(xn,yn), the formula for computing the correlation coefficient is given by:

## Slide 59: Linear correlation

## Slide 60: Linear correlation

## Slide 61: Secant method
The secant method is a root-finding algorithm that uses a succession of roots of secant lines to better approximate a root of a function f.
The secant method is defined by the recurrence relation:

## Slide 62: Secant method

## Slide 63: Secant method

## Slide 64: Secant method

## Slide 65: Image understanding
Homework assignment 2

## Slide 66: Brightness adjustment

## Slide 67: Brightness adjustment

## Slide 68: Machine learning
Homework assignment 3

## Slide 69: Perceptron

## Slide 70: Perceptron

## Slide 71: Tensor calculus

## Slide 72: Q&A