## Slide 1: A Survey of Split Data Caches
Authors: Miroslav Gašić, gmikamg@yahoo.com Prof. dr Veljko Milutinović, vm@etf.bg.ac.yu

## Slide 2: Summary
1. Introduction
2. Classification and design issues
3. Case studies
Hm cache memory…

## Slide 3: Introduction
1. Memory gap
2. Cache concepts
3. Why split?

## Slide 4: Memory gap
Difference in speed between processor and memory
Steadily increasing
Major problem (since the beginning of 1990’s)
The average number of machine cycles per instruction has also been decreasing – this effect and the effect of speed difference are multiplicative
Example of increase in memory access cost – time of a full cache miss in instructions executed
  1st Alpha (7000): 340 ns/5.0 ns = 68 clks x 2 or 136 instructions
  2nd Alpha (8400): 266 ns/3.3 ns = 80 clks x 4 or 320 instructions
  3rd Alpha (t.b.d.): 180 ns/1.7 ns =108 clks x 6 or 648 instructions

## Slide 5: Memory gap
µProc
60%/yr.
(2X/1.5yr)
DRAM
9%/yr.
(2X/10 yrs)
1
10
100
1000
1980
1981
1983
1984
1985
1986
1987
1988
1989
1990
1991
1992
1993
1994
1995
1996
1997
1998
1999
2000
DRAM
CPU
1982
Processor-Memory
Performance Gap: (grows 50% / year)
Performance
Time
“Moore’s Law”
Processor-DRAM Memory Gap (latency)

## Slide 6: Introduction
1. Memory gap
2. Cache concepts
3. Why split?

## Slide 7: Cache concepts
Purpose – to bridge the memory gap (i.e., hide memory latency) and reduce the demand bandwidth on the main memory
Locality – temporal and spatial
Associativity – direct-mapped, set associative, fully associative
Block size (sometimes called line size)
Miss rate
Miss types – capacity, coherence, compulsory, and conflict

## Slide 8: Cache concepts
Usually organized as a multiple level hierarchy
The first-level hierarchy is split into two independent organizations – one for storing instructions and another for storing data
Differences in behavior of instructions (mostly spatial,…) and data (both spatial and temporal)
We will only consider data caches

## Slide 9: Cache concepts
To illustrate both specialization and a multi-level caching, we show here the cache hierarchy of the AMD Athlon 64

## Slide 10: Introduction
1. Memory gap
2. Cache concepts
3. Why split?

## Slide 11: Why split?
Data exhibit different kinds of locality
Conventional cache organizations do not distinguish different types of locality and non-selectively cache all data
This causes:
  Unnecessary movement of data among the levels of the memory hierarchy
  Significant interference between unrelated data inside cache
  Bringing of useless data into cache, thus causing removal of potentially useful data, thus causing cache pollution
Consequences of that kind of behavior are increases in:
  Miss ratio
  Memory access time
  Memory bandwidth
Idea 1: Make two or more sets of data exhibiting same characteristic or property

## Slide 12: Why split?
Different kinds of localities and data types have different demands – in the sense of cache organization, treatment…
For exploiting of temporal locality better smaller blocks, for spatial locality better larger blocks
For data exhibiting spatial locality prefetching is very useful, for data exhibiting temporal locality prefetching is useless and can cause some serious problems (already mentioned)
It is not possible to design a single cache that works well for different types of localities and data types
Idea 2: If it is not possible to design a single cache that works well for different types of localities and data types, design multiple data caches with different organizations. Each subset of data is put in one of the caches (called subcaches)

## Slide 13: Summary
1.Introduction
2.Classification and design issues
3.Case studies

## Slide 14: Classification and design issues
1. Classification
2. Design issues

## Slide 15: Classification
Because of great variety of solutions and ideas, among different designs, it is very hard to classify them in homogenous sets – classification is very rough
The classifications to be given extracts same things, among different designs, and in this way helps us to remember all those different designs and their basic characteristics
If two designs belong to the same group it does not imply that there are very similar i.e., there may or may not be great similarity among them

## Slide 16: Classification
The reuse information gathers the behavior of the stored cache blocks in L1 (level 1 cache)
Decision in which subcache to place the block is made with the help of this information
It can be stored in L2 (level 2 cache) or in a assistant TRI (table reuse information) table
Some designs manage reuse information and some do not:
  Managing Reuse Information:
    Dual Data Cache, STS, NTS, SSNS, LSM, Filter Data Cache
  Non-Managing Reuse Information:
    Victim cache, Assist Cache, Allocation by Conflict Scheme

## Slide 17: Classification
Subcaches can have different organizations, i.e., they can have different associativity or block size (in order to better exploit different characteristics data exhibit)
Some designs have different associativity some have different block sizes, among subcaches:
  Different associativity with same block sizes:
    Victim cache, Assist cache, NTS, minimax, Intel StrongARM SA-1110 (last two are for embedded processors)
  Same associativity with different block sizes:
    Dual Data Cache, STS, SS/NS, Array/Scalar

## Slide 18: Classification and design issues
1. Classification
2. Design issues
Niagara processor micrograph

## Slide 19: Design issues
Decisions designer has to make:
  The characteristics of the data that will be placed in each subcache
  The cache organization
  The datapath connecting both subcaches
  So on…
Process of designing is usually not sequential – because the steps can interact with each other
We will define process that is simple, sequential, and easy to understand

## Slide 20: Design issue
Design process divided in four main steps:
  1. Specifying the types of data – designer divides the data in sets each to be set in a specific cache organization
  2. Deciding when to classify the data and how the scheme will work:
    Software-tagging schemes:
      Compiler predicts data behavior
      It is very difficult for the compiler to predict correct data behavior
    Tagging at runtime schemes:
      According to dynamically observed changing access patterns
      Sometimes the compiler helps the hardware by inserting hints
      Preferable
      Requires extra hardware:
        For classifying and labeling data
        For placing the label (reuse) information

## Slide 21: Design issue
Figure showing typical L1 split cache using reuse information:
Tags
and
data
Current
usage
information
Tags
and
data
Current
usage
information
?
Tags
Data array
Reuse
information
Level-two cache
Level-one cache
Level-one cache miss
Level-two cache hit
We use Reuse information to decide where to put data
Notice: additional datapath connecting both L1 data caches (not appearing in all schemes)

## Slide 22: Design issue
  3. Tuning the cache characteristics:
    Matching of the data characteristics with the specific cache geometry:
        Cache size
        Block size
        Placement and replacement algorithms (usually LRU)
    Additional techniques can be used – prefetch
    Decoupled subcaches or datapath between them
  4. Checking the idea:
    Analytical model
    Run simulations

## Slide 23: Summary
1. Introduction
2. Classification and design process
3. Case studies
Yes…I can see what is going to be the locality of that data

## Slide 24: Case studies
1. Case studies presentation outline
2. The victim cache
3. The dual data cache (dual)
4. The split temporal spatial cache (STS)
5. The assist cache (assist)
6. The nontemporal streaming cache (NTS)
7. The scalar-array data cache (array)
8. The filter cache (filter)
9. The split spatial nonspatial cache (SS/NS)
10. Conclusion

## Slide 25: Case studies presentation outline
Design presentations will be based on the following pattern, except for minor changes in some cases, where such (a little bit) different pattern is more appropriate:
  Idea
  Organization of the design
  The way it works
  Block diagram of the design (animation of functioning)
  Similarities with some other designs
  Performance results

## Slide 26: Case studies
1. Case studies presentation outline
2. The victim cache
3. The dual data cache (dual)
4. The split temporal spatial cache (STS)
5. The assist cache (assist)
6. The nontemporal streaming cache (NTS)
7. The scalar-array data cache (array)
8. The filter cache (filter)
9. The split spatial nonspatial cache (SS/NS)
10. Conclusion

## Slide 27: The victim cache [1]
Performance of direct-mapped caches is better than that of set-associative caches, in spite of a higher number of conflict misses
The idea was to remove some percent of those conflict misses
How to achieve that?
Conflict misses are due to the lack of associativity
Conclusion was to add a small, fully associative (victim) cache, next to the direct-mapped (main) cache, and in this way to increase associativity
The victim scheme is a large direct-mapped cache with a small, fully associative cache next to it
Associative cache (buffer) goal is to retain the most recent conflict lines

## Slide 28: The victim cache
How this scheme works:
  Hit in main cache – access proceeds as normal
  Miss in main cache, hit in small subcache – lines in main cache and victim cache are swapped
  Miss in both caches – referenced line from L2 to main cache, conflict from main victim cache
Similar organization to that in the Assist cache – difference is datapath connecting both subcaches

## Slide 29: The victim cache
Paper [1] also introduced stream buffers and multi-way stream buffers – hardware prefetching techniques, the main goal of which is to reduce capacity and compulsory (cold start, etc.) misses
The main problem of standard prefetching algorithms, (prefetch always, prefetch on miss, and tagged prefetch) which stream buffers aim to solve, is too much time till prefetch returns
Stream buffers also avoid cache pollution
Since data references tend to consist of interleaved streams of data from different sources multi-way stream buffers were also introduced

## Slide 30: The victim cache
In the pictures above on the left you can see stream buffer design and on the right four-way streambuffer design

## Slide 31: The victim cache
Tags
Data
Address from processor
Data to processor
Address to next lower cache
Data from next lower cache
Direct-mapped cache
Fully-associative victim cache
LRU entry
MRU entry
:
: :
:
: :
:
: :
:
: :
Miss in the main cache
Miss in the victim cache
LRU entry evicted to the lower cache
MRU entry
LRU entry
tag
tag
tag
tag
comparator
comparator
comparator
comparator
one cache line of data
one cache line of data
one cache line of data
one cache line of data
The conflict block is put in the victim cache
The referenced line is put in the main cache
Miss in both main and victim cache:

## Slide 32: The victim cache
The figure above shows the percent of conflict misses removed by the victim scheme – the figure is taken from [1]
Notice that victim caching improves D-cache (data cache) miss rate much more than I-cache (instruction cache) miss rate

## Slide 33: Case studies
1. Case studies presentation outline
2. The victim cache
3. The dual data cache (dual)
4. The split temporal spatial cache (STS)
5. The assist cache (assist)
6. The nontemporal streaming cache (NTS)
7. The scalar-array data cache (array)
8. The filter cache (filter)
9. The split spatial nonspatial cache (SS/NS)
10. Conclusion

## Slide 34: The dual data cache [2]
Two main reasons for loss of performance are:
  The use of the same organization for caching both spatial and temporal locality data
  “Eager” caching policy used by caches
Cache line size are a few tens of bytes in conventional caches – memory reference patterns with low spatial locality cause pollution
Data are always cached – this can cause swept of the cache without opportunity to exploit temporal locality
How to solve mentioned problems?
Two independent caches: temporal and spatial cache
The spatial cache exploits spatial and temporal locality
The spatial cache can incorporate some prefetch technique
The temporal cache exploits just temporal locality

## Slide 35: The dual data cache
Where to put data?
Locality prediction table (LPT) – history table with information about the most recently executed load/store instructions (arranged at runtime)
The prediction where to place data can be:
  Spatial – the data are cached in the spatial cache
  Temporal – the data are cached in the temporal cache
  Bypass – the data are not cached
  Default value – the data are cached in the predefined cache, the simulations showed that the most effective default value is temporal
The line size of the spatial cache – several tens of bytes or more
The line size of the temporal cache – a few bytes

## Slide 36: The dual data cache
How this scheme works:
  If the data is only in one of the subcaches, the data is read or written in that subcache
  If the data is found in both subcaches, it is read from temporal cache or written in both two in parallel
  If the data is not in any of the subcaches, a cache miss occurs, data is brought from the next level of the memory hierarchy, and further is treated in the way prediction says
It has similar organization to the STS cache – but differences and similarities we will consider in the part about the STS cache
In paper [2] a selective cache was also introduced – this cache consists of the same prediction table, but it only has one memory unit like a conventional caches (it behaves as a conventional cache with selective caching policy)

## Slide 37: The dual data cache
Miss in both spatial and temporal cache:
Spatial
Cache
Temporal
Cache
Program
Counter
Locality
Prediction
Table
memory request from CPU
data from L2 cache
data to/from CPU
hit_s
hit_t
hit/miss
to L2 cache
hit_s
hit_t
Miss
Miss in the both subcaches
In LPT it can be both hit or miss
Depending of prediction it is decided where to put data
Hit in the spatial cache

## Slide 38: The dual data cache
Simulations were performed for different configurations with similar hardware cost:
  A conventional cache of size S
  A dual data cache with temporal cache of size S/4, and spatial cache of size S/4, the remaining amount of storage is dedicated to the LPT (less than S/4, because of greater demands for tag memory required in case of the dual data cache)
  A selective cache of size S – the LPT is much simpler than in case of the dual data cache so it is not taken into account
The dual data cache outperformed a conventional cache in many cases – exception were benchmarks where almost all memory references exhibit spatial locality
Even the selective cache is always better than conventional cache with a very few exceptions

## Slide 39: Case studies
1. Case studies presentation outline
2. The victim cache
3. The dual data cache (dual)
4. The split temporal spatial cache (STS)
5. The assist cache (assist)
6. The nontemporal streaming cache (NTS)
7. The scalar-array data cache (array)
8. The filter cache (filter)
9. The split spatial nonspatial cache (SS/NS)
10. Conclusion

## Slide 40: The split temporal spatial cache (STS) [3][4][5]
Conventional cache systems imply no separation of data based on their locality – not optimal
Separate cache in two parts and employ a different internal organization, for better utilization of data characteristics
“Spatial” part – data exhibiting spatial locality
“Temporal” part – data exhibiting temporal locality
Locality resolving – different algorithms for tagging and retagging of data
Algorithms for tagging and retagging of data:
  The compile-time algorithms – the simplest one labels the simple variables and constants as temporal and the complex and structured data type as spatial
  The profile-time algorithm – initially all regarded as spatial, then each block associated with two counters – one to count the number of the processor references to block and the other to test if temporal locality appears
  The run-time algorithm – differs from the profile-time algorithm only in possibility for retagging the temporal block again to spatial

## Slide 41: The split temporal spatial cache (STS)
The code above shows the run-time algorithm for data tagging and retagging– the profile time algorithm only has additional if condition (if (Tag=Spatial)) to disable retagging of data from temporal to spatial
Hardware for implementation of the run time algorithm is shown on the picture up – picture is taken from [3]
if(hit.in.block)
{ if(-X<Xcount<X)
if(Hi) Xcount=Xcount+1;
else Xcount=Xcount-1;
if(Ycount<Y) Ycount=Ycount+1;
else { if(-X<Xcount<X) Tag=Spatial;
else Tag=Temporal;
Xcount=0;
Ycount=0;
}
}

## Slide 42: The split temporal spatial cache (STS)
“Spatial” part :
  Relatively small and fast one-level cache with a usual block size (NOTICE: does not have second level cache)
  Incorporated hardware implemented prefetch mechanism
“Temporal” part:
  A usual two-level hierarchy
  One-word block size (both for the first and the second level cache) – since there is no spatial locality
L2 cache is much smaller than a conventional L2 cache – suitable for integration on processor chip

## Slide 43: The split temporal spatial cache (STS)
How this model works:
  Request from processor is sent to all STS cache modules at the same time
  Hit in one of the part (temporal or spatial) – signal to other part of the STS to prevent its request to the main memory
  In case of miss in some STS module eviction is prepared (if dirty)
  Hit in spatial module aborts activities of temporal module and vice versa
  T1C miss, T2C hit – data are also written into T1C
  Miss in all modules – memory fetch initiated
  Depending from tag, block is placed into spatial or temporal part
  Fetch into temporal part loads both T1C and T2C
  If the block is written into SC, next block is also prefetched (if not already present in spatial part)

## Slide 44: The split temporal spatial cache (STS)
CPU
SC
T1C
T2C
MM
PFL
WB
T1C Hit
T2C Hit
SC Hit
WB
WB
MFC
CPU – processor
PFL – prefetching logic
SC – spatial part
WB – write buffers
T1C and T2C – first and second level in temporal part
MM – main memory
SC Hit, T1C Hit, and T2C Hit – hit detection signals
MFC –“memory function completed” signal sent by memory
Miss in the T1C
Miss in the SC
Hit in the T2C
Miss in T1C and SC hit in T2C:
Stops activity of the SC
Data send from the T2C to the T1C
Evicted data written to the T2C

## Slide 45: The split temporal spatial cache (STS)
Similarities with the dual data cache – two parts of cache (temporal and spatial) with different block sizes and prefetching possibility in the spatial part
Differences with the dual data cache – temporal part two-level hierarchy, run time mechanism for detection of data locality very different

## Slide 46: The split temporal spatial cache (STS)
The figure up shows average memory latency of two variants of STS design and classic design – figure is taken from [5]
STS1 R5 – equal spatial and temporal primary subcaches, locality decisions is made at runtime and threshold for X and Y counters are set to five
STS1 P5 – same as STS1 R5 only locality decision is made at profiling time
Classic – primary cache equals to the sum of capacities of STS subcaches and a secondary cache equals twice the secondary temporal cache of STS
Results shown on this figure are the one in which the difference of the STS performance is not so obvious, as in other results of performance

## Slide 47: Case studies
1. Case studies presentation outline
2. The victim cache
3. The dual data cache (dual)
4. The split temporal spatial cache (STS)
5. The assist cache (assist)
6. The nontemporal streaming cache (NTS)
7. The scalar-array data cache (array)
8. The filter cache (filter)
9. The split spatial nonspatial cache (SS/NS)
10. Conclusion

## Slide 48: The assist cache (assist) [6]
The assist cache is incorporated in HP-7200
Assist cache is fully associative on-chip cache – 64 cache lines each 32-byte in size
Processor also contains an interface to up to 1M byte of off-chip direct-mapped data cache
On-chip cache + off-chip cache = level-1 cache
Level-1 cache is large and accessed at one processor cycle – no level-2 cache supported

## Slide 49: The assist cache (assist)
One of the goals was to eliminate thrashing that can occur with a direct-mapped cache
Example:
for i: = 0 to N do
A[i]:= B[i] + C[i] +D[i]
If elements map to the same cache index eight iterations cause 32 cache misses
With assist cache eight iterations can cause only initial 4 cache misses
Larger caches do not reduce this type of cache thrashing
Spatial locality only hint can be specified in load and store instructions to indicate that data exhibits spatial but not temporal locality – encoded in previously reserved load and store instruction fields
Line containing the spatial locality only hint upon replacement is flushed back to memory – avoiding the off-chip cache pollution

## Slide 50: The assist cache (assist)
Data prefetching:
  Instructions which can help to speculate what data may soon be accessed by code stream
  Example:
  LDWX,m r1(r2),r3 – this instruction does following
  load [r2] →r3; r1+r2→ r2, for example if r1=0x40 and r2=0x100 the line containing 0x140 will be prefetched. Prefetched line is moved into the assist cache and tagged as being prefetched line. When a prefetched line is later referenced by the code stream, another prefetch is launched. Continuing with the above example if in some loop 0x140 is referenced than line containing 0x180 will be prefetched and so on
Instruction set tailored to benefit memory hierarchy

## Slide 51: The assist cache (assist)
How does this scheme work:
  For each cache access, 65 entries are checked for a valid match – 64 assist cache entries and one off-chip cache entry
  Lines requested from memory, as a result of cache miss or prefetches, are initially moved to assist cache
  Lines that are moved out of the assist cache can conditionally bypass the off-chip cache and move directly back to memory (spatial locality only hint used for making decision)
  Lines are moved out of the assist cache in first-in, first-out order

## Slide 52: The assist cache (assist)
Hash
Memory Interface
TLB
Physical Address
Virtual Address
Physical tag
32-byte Data Line
Assist cache
Virtual Address
Data to/from Functional Units
Main cache
Physical Tag
32-Byte Data Line
Miss in assist and off-chip cache:
Miss in the main cache
Miss in the assist cache
First-in line to be replaced (contains spatial locality only hint)
Sent memory request
Memory reply
New line is put in cache
Line to be replaced sent to memory

## Slide 53: The assist cache (assist)
Figure above is taken from [7] it shows the performance of PA 7200 CPU compared to PA 7100
A number of features that minimize the average memory access time allow HP PA 7200 to outperform its predecessor on technical benchmarks
NOTICE: usage of the assist cache wasn’t only improvement

## Slide 54: Case studies
1. Case studies presentation outline
2. The victim cache
3. The dual data cache (dual)
4. The split temporal spatial cache (STS)
5. The assist cache (assist)
6. The nontemporal streaming cache (NTS)
7. The scalar-array data cache (array)
8. The filter cache (filter)
9. The split spatial nonspatial cache (SS/NS)
10. Conclusion

## Slide 55: The nontemporal streaming cache (NTS) [7]
Reduce conflict misses in direct-mapped caches
Supplement a conventional direct-mapped cache with a parallel fully associative buffer to reduce conflict misses
Every cache block, loaded into the main cache, is monitored for temporal behavior by a hardware detection unit
Cache blocks identified as nontemporal are allocated to the buffer on subsequent requests, temporal blocks are allocated in the main cache
Consideration of block conflict problem?

## Slide 56: The nontemporal streaming cache (NTS)
Required second level cache
The NTS structure divided into two parts:
  Data storing unit (DSU) – direct-mapped cache and an LRU managed fully associative NT buffer
  Nontemporal data detection unit (NTDU) – matrix of bits with breadth equal to the number of words in a cache block, and depth equal to the number of sets in the main cache
Each block in the main cache and the secondary cache carries an NT bit – used to decide where a block, that misses in the DSU but hits in the secondary cache, should be allocated in the DSU
NT buffer and the main cache are probed in parallel

## Slide 57: The nontemporal streaming cache (NTS)
The NTDU monitors the reuse behavior of block in the main cache
When a block leaves the main cache, if no element has been referenced during his cache lifetime, the block is marked as NT; otherwise, the NT bit is left in its prior state
NT preserved in secondary cache but not in main memory
Important notice:
  A block can have its NT set during any main cache lifetime
  An NT tag set is never reset until the block is replaced in the secondary cache

## Slide 58: The nontemporal streaming cache (NTS)
How this scheme works:
  Main cache hit and NT buffer miss – delivery of data, update of the NTDU and the NT bit
  Main cache miss and NT buffer hit – only delivery of data nothing else is needed
  Main cache miss, NT buffer miss, and secondary cache hit – based on the block’s NT bit decide where to put data, initialize the NTDU if needed
  Main cache miss, NT buffer miss and secondary cache miss – block placed in main cache, the NTDU and NT bit reset

## Slide 59: The nontemporal streaming cache (NTS)
NTDU
….
….
….
….
….
….
Physical Address
Data To/From Functional Unit
NT Buffer
Main Cache
Tag
Cache Block Data
NT bit
NT bit
Cache Block Data
L2 Cache Block Data
Tag
Tag
Full NTS Structure
Secondary Cache
Miss in main cache and NT buffer, hit in secondary cache:
Miss in the main cache
Miss in the NT buffer
Hit in the secondary cache (NT bit is reset so goes to the main cache)
Conflict block evicted to secondary cache
Initialized to standard value
Hit in the main cache
Miss in the NT buffer

## Slide 60: The nontemporal streaming cache (NTS)
The table up shows comparison of MPCR (mean cost per reference) parameter for different configurations of standard DM cache and NTS cache – table is taken from [7]

## Slide 61: Case studies
1. Case studies presentation outline
2. The victim cache
3. The dual data cache (dual)
4. The split temporal spatial cache (STS)
5. The assist cache (assist)
6. The nontemporal streaming cache (NTS)
7. The scalar-array data cache (array)
8. The filter cache (filter)
9. The split spatial nonspatial cache (SS/NS)
10. Conclusion

## Slide 62: The scalar-array data cache (array)
Pretty similar ideas like in previous works we will repeat them here again in short
Locality can be either temporal or spatial
Yet most accesses are both spatial and temporal
But accesses to some data structures, such as arrays, tend to be more often spatial while accesses to scalar variables tend to be more temporal
Spatial locality benefits from large, but fewer cache blocks, while temporal locality is best exploited by many, but smaller cache blocks

## Slide 63: The scalar-array data cache (array)
In this organization we have separated array and scalar caches
All arrays are stored in an array cache and scalars in a scalar cache
Array and scalar references are tagged as such by the compiler, using different op-codes, and are directed to the respective caches

## Slide 64: The scalar-array data cache (array)
How this scheme work:
  Hit in scalar cache – it proceeds as normal
  Hit in array cache – it proceeds as normal
  Miss in both subcaches – according to the tag, provided by the compiler, demanded data are put either in array or scalar cache
This scheme has some similarities with the schemes preceding it the dual data cache and STS scheme

## Slide 65: The scalar-array data cache (array)
Miss in both caches:
Data bus
Address bus
Cache selection
Scalar Data Cache
Array Data Cache
CPU
Lower memory levels
Miss in the array cache
The array cache is selected
Once again the same request from the CPU
Because array cache is selected the data are brought in it
Hit in the array cache

## Slide 66: The scalar-array data cache (array)
On the picture above we can see weighted average of all benchmark
Note that miss does not cost same for different block size

## Slide 67: Case studies
1. Case studies presentation outline
2. The victim cache
3. The dual data cache (dual)
4. The split temporal spatial cache (STS)
5. The assist cache (assist)
6. The nontemporal streaming cache (NTS)
7. The scalar-array data cache (array)
8. The filter cache (filter)
9. The split spatial nonspatial cache (SS/NS)
10. Conclusion

## Slide 68: The filter cache (filter) [8]
Detect blocks most heavily referenced
Counter attached to each block in all caches
Block referenced a lot of times –there is a high probability that the block data exhibit both localities

## Slide 69: The filter cache (filter)
Focuses on multiprocessor system – forth kind of miss (the coherence miss) and bus utilization problem
Also can be applied to uniprocessor systems
Two independent caches in the first level cache – the main cache (MC) and the filter cache (FC)
A common second level cache – takes care of coherence maintenance
All the cache blocks incorporate a counter in order to keep track of the access frequency of the block
Lookup in both L1 data caches (MC and FC) is performed in parallel

## Slide 70: The filter cache (filter)
How does this model work:
  Hit in any of the two caches – corresponding counter incremented, data delivered
  Miss in both L1 caches – blocked fetched from the higher level in the hierarchy . A candidate block to be replaced in the filter cache is chosen. The counter value of the missing block (ctr_miss) compared with the counter value of the candidate block (ctr_candidate). If (ctr_miss>ctr_candidate) the missing is moved into the filter cache, else it is moved into the main cache. In the first case replaced block is moved into the main cache if its counter value is greater than one. When a block is replaced from the main cache its counter value is flushed into the L2 cache

## Slide 71: The filter cache (filter)
To the Bus
CPU
L2 CACHE
(Tags and data)
Main Cache
(Tags and data)
Counters
Counters
Counters
Filter cache
(Tags and data)
Miss in both L1 caches, hit in L2 cache:
Miss in main cache
Miss in filter cache
Hit in L2 cache
Compared ctr_miss and ctr_candidate (ctr_miss>candidate)
Moved to L2 cache
Move to main cache
Move to filter cache

## Slide 72: The filter cache (filter)
Relative Speedups over a Conventional Organization
For multiprocessor systems the bus utilization and the speedup are more relevant than the mean data access time
As the number of processor increases the performance of purposed model improves compared to conventional model

## Slide 73: Case studies
1. Case studies presentation outline
2. The victim cache
3. The dual data cache (dual)
4. The split temporal spatial cache (STS)
5. The assist cache (assist)
6. The nontemporal streaming (NTS)
7. The scalar-array data cache (array)
8. The filter cache (filter)
9. The split spatial nonspatial cache (SS/NS)
10. Conclusion

## Slide 74: The Split Spatial Nonspatial Cache (SS-NS)
Utilization of cache splitting and prefetching in order to exploit any degree of spatial locality
Also the idea was to solve drawbacks of STS cache
Which are those drawbacks and what solution were purposed?
Varying thresholds for X and Y counter between different applications
Different method of spatial locality detection – flag-based
Once the data is declared temporal, there is no way for it to be declared spatial again
Way to detect spatial locality in the temporal subcache and place that block in the spatial subcache
Also simulations showed that a second level cache is needed in the spatial part of the STS

## Slide 75: The Split Spatial Nonspatial Cache (SS-NS)
Organization of the design is following:
  The primary cache is split into two subcaches, according to the spatial locality of data
  The non-spatial cache consists of blocks (called sub-blocks) that are one word (eight bytes wide) – intended to cache data words exhibiting no useful spatial locality
  The spatial subcache consists of blocks (called blocks) that are 32 bytes (four words) wide – intended to cache the data words exhibiting useful spatial locality

## Slide 76: The Split Spatial Nonspatial Cache (SS-NS)
The flag-based method of spatial locality detection:
  Each block in the spatial subcache is associated with four bits (one for each word in the block)
  These bits are initialized to zero when the block is fetched into the cache, and each bit is set when the corresponding word has been accessed
  If less than two of these four bits are set, the block exhibits no useful spatial locality – and therefore is marked as non-spatial

## Slide 77: The Split Spatial Nonspatial Cache (SS-NS)
The main ideas behind the new way of detecting spatial locality in non-spatial subcache:
  If two or more sub-blocks are parts of the same block are present in the non-spatial subcache, then this block should be marked as spatial and caches in the spatial subcache
  Since caching spatial blocks in the non-spatial subcache causes a miss whenever a new sub-block of that block is accessed, we want to stop caching such blocks in non-spatial cache as soon as they are detected to be spatial

## Slide 78: The Split Spatial Nonspatial Cache (SS-NS)
How does detection process look:
  Each miss in the non-spatial subcache invokes a search for the other sub-blocks that belong to the same block as the missed sub-block
  If any such sub-block is found, the block is marked as spatial and a fetch of the entire block into the spatial subcache is initiated
  The one sub-block that was found in the non-spatial cache is transferred into the newly allocated block in the spatial cache and invalidated in the non-spatial cache

## Slide 79: The Split Spatial Nonspatial Cache (SS-NS)
In the spatial part various prefetching methods may be implemented – purposed one are “always”, “flag” and “bi-directional”
The secondary cache is not split in order to keep the design relatively simple
The secondary cache uses one bit to keep the information about locality of the block
For data that are not present in the secondary cache, one-bit spatial locality predictor can be used

## Slide 80: The Split Spatial Nonspatial Cache (SS-NS)
How this scheme works:
  Hit in non-spatial part – it proceeds as normal
  Hit in spatial part – depending on the prefetching logic prefetch is made or not, the rest proceeds as normal
  Miss in both spatial and non-spatial subcache – in the case that the sub-block belonging to the same block is not found (in non-spatial part) the data is brought from the lower levels of memory hierarchy and placed in one of the subcaches according to the locality information or prediction, in other case it proceeds as described in previous slide (slide 77)
  Because there can not be hit at the same time in both subcaches with described situations all cases are covered

## Slide 81: The Split Spatial Nonspatial Cache (SS-NS)
Miss in both subcaches:
Spatial
locality
predictor
CPU
Spatial
cache
Nonspatial
cache
Operating memory
L2 cache
PFL
flags
Miss in the nonspatial cache
Miss in the spatial cache
Miss in L2 cache
It is predicted that the data will be spatial
Hit in the spatial cache
Appropriate flag is set

## Slide 82: The Split Spatial Nonspatial Cache (SS-NS)
On the pictures above we can see average memory latency and average bus traffic for different cache designs

## Slide 83: Design presentations
1. Design presentation outline
2. The victim cache
3. The dual data cache (dual)
4. The split temporal cache (STS)
5. The assist cache (assist)
6. The nontemporal streaming (NTS)
7. The filter cache (filter)
8. Conclusion

## Slide 84: Conclusion
Each scheme offers better performance than a conventional organization with similar size
Usually, schemes use a larger main cache and a much smaller buffer cache
Reevaluation needed
Trade-off between complexity and performance

## Slide 85: References
[1] N.P. Jouppi, “Improving Direct-Mapped Cache Performance by the Addition of a Small Fully Associative Cache and Prefetch Buffers”, Proc. Int’l Symp. Computer Architecture, ACM Press, New York, 1990, pp. 364-373.
[2] A. Gonzalez, C. Aliaga, and M. Valero,”A Data Cache with Multiple Caching Strategies Tunes to Different Type of Locality,” Proc. Int’l Conf. Supercomputing, ACM Press, New York, 1995, pp. 383-347.
[3] V. Milutinović, B. Marković, M. Tomašević, and M. Tremblay, “The Split Temporal/Spatial Cache: Initial Performance Analysis,” Proc. SCIzzL-5, Mar. 1996, pp. 338-347.
[4] V. Milutinović, B. Marković, M. Tomašević, and M. Tremblay, “The Split Temporal/Spatial Cache: A Complexity Analysis,” Proc. SCIzzL-6, Sept. 1996, pp. 89-96.
[5] M. Prvulović, D. Marinov, V. Milutinović, “A Performance Reevaluation of the Split Temporal/Spatial Cache ,” Workshop Digest of the PAID/ISCA-98, Barcelona, Spain, June 1998.

## Slide 86: References
[6] K.K. Chan et al., ”Design of the HP PA 7200 CPU,” Hewlett-Packard J., Feb. 1996, pp. 1-12.
[7] J.A. Rivers and E.S. Davidson, “Reducing Conflicts in Direct-Mapped Caches with a Temporality-Based Design,” Proc. 1996 Int’l Conf. Parallel Processing, IEEE Computer Soc. Press, Los Alamitos, Calif., Aug. 1996, pp. 151-160
[8] J. Sahuquillo and A. Pont, ”The Filter Cache: A Runtime Cache Management Approach,” Proc. 25th Euromicro Conf., 1999, IEEE Computer Soc. Press, Los Alamitos, Calif., pp. 424-431.