## Slide 1: Introduction to SystemC
Darko Jović

## Slide 2: Design Process Today
C/C++ Environment
System Level Design
  Hardware and Software
  Algorithm Development
  Processor Selection
  Done mainly in C/C++
EDA Environment
IC Development
  Hardware
  Implementation Decisions
  Done mainly in Verilog/VHDL
C/C++ Environment
Software
  Code development
  RTOS details
  Done mainly in C/C++
Refinement
Refinement
Manual Translation
$ $
Emulation /
Prototyping
The Verification Process
Productivity Gaps

## Slide 3: IC Development Process

## Slide 4: HDL Based Flow
C/C++
1. Conceptualize
2. Simulate in C++
3. Write specification
document
4. Hand over specification document
HDL
5. Understand
6. (Re)Implement in HDL
7. (Re)Verify
8. Synthesize from HDL
Problems:Written specifications are incomplete and inconsistent
Translation to HDL is time consuming and error prone

## Slide 5: C++ Based Flow
C/C++
1. Conceptualize
2. Simulate in C++
3. Write specification
document
4. Hand over
  Executable specification
  Testbench
  Written specification
C/C++
5. Understand
6. Refine in C++
7. Verify reusing testbenches
8. Synthesize from C++
Turning Algorithms into the Right Architectures for ASICs
quicker and better

## Slide 6: Why C/C++ Based Design
Specification between architect and implementer is executable
High simulation speed at the higher level of abstraction
Refinement, no translation into HDL (no “semantic gap”)
Testbench re-use
SoC Design
System
Architect
C/C++
Software
Designer
C/C++
Hardware
Designer
HDL
Marketing
& Sales

## Slide 7: Can C++ be used as is?
Languages such as C/C++ and Java are not created to model hardware
Not supported by native C/C++:
  Hardware style communication
    Signals, protocols, …
  Notion of time
    Cycle/clock, delay, time sequenced op., ...
  Concurrency
    Hardware and systems are inherently concurrent
  Reactivity
    Hardware responds to stimuli and is in constant interaction with its environment
  Hardware data types
    Bits, bit-vector types, multi valued logic type, and so on

## Slide 8: What is SystemC?
C++ class library + simulation kernel, which supports hardware modeling concepts at system level, behavioral level, RTL level
Provides hardware style communication, notion of time, concurrency, reactivity, and hardware data types
Methodology for modeling SoC designs consisting DSPs, ASICs, IP Cores, Interfaces, …
Enables modeling at high level of abstraction e.g. communication protocols
Enables refinement to hardware
Enables software modeling: interrupts, exception handling
Enables system wide verification
Enables HW/SW co-verification
Enables IP exchange

## Slide 9: SystemC Features
Processes <- for concurrency
Clocks <- for time
Hardware data types: bit vectors, 4-valued logic, fixed-point types, arbitrary precision integers
Waiting and watching <- for reactivity
Modules, ports, and signals <- for hierarchy
Channel, interface, and event <- abstract communication

## Slide 10: SystemC History
September 1999: SystemC launched with OSCI (Open SystemC Initiative: www.SystemC.org)
September 1999: SystemC v0.9
February 2000: SystemC v0.91
March 2000: SystemC v1.0 (fixed-point package added)
June 2000: SystemC v1.1B
2000: SystmC v1.2B
October 2001: SystemC v2.0
2002: SystemC v2.0.1
June 2005. SystemC v2.1
December 12. 2005. SystemC IEEE 1666 standard

## Slide 11: SystemC Design Environment
class library
and
simulation kernel
source files for system
and testbenches
your standard
C/C++ development
environment
compiler
linker
debugger
libraries
header files
„executable
specification“
.......
....
executable = simulator
a.out
„make“
ASIC
IP-Core
Interface
DSP

## Slide 12: SystemC Components
User libraries |  | SCV |  | Other IP | 
Predefined Primitive Channels: Mutexs, FIFOs & Signals |  |  |  |  | 
Simulation Kernel | Threads & Methods |  | Channels & Interfaces |  | Data types: Logic, Integers, Fixed point
 | Events, Sensitivity & Notification |  | Modules & Hierarchy |  | 
C++ |  |  |  |  | STL

## Slide 13: Data Types
C++ built in data types may be used but are not adequate to model Hardware.
  long, int, short, char, unsigned long, unsigned int, unsigned short, unsigned char, float, double, long double, and bool
SystemCTM provides other types that are needed for System modeling.
  Boolean types: sc_bit
  Scalar types: sc_logic
  Integer types: sc_int<length>, sc_uint<length>, sc_bigint<length>, sc_biguint<length>
  Logic/Boolean vector types: sc_bv<length>, sc_lv<length>, sc_array

## Slide 14: Data Types
There is a tradeoff between simulation speed and code objective.
To summarize, follow these rules in order:
    use native data types as much as possible
    use sc_int<length>/sc_uint<length>
    use sc_bv<length> for bitwise operations
    use sc_logic/sc_lv<length> to model 'X' and 'Z’
    use sc_bigint<length>/sc_biguint<length> for arbitrary length arithmetic operations
Fastest
Slowest

## Slide 15: Data Types
sc_int<length>, sc_uint<length>
  Used for performing arithmetic on signed and unsigned integers of less than or equal to 64 bits (on a 32-bit machine)
  Not optimal for bit vector manipulation
  A two's-complement representation is used for signed integers
  An array of bits
      Can address an individual bit
      Interpreted as an integer for arithmetic operations
  Simulate faster than the arbitrary precision data types

## Slide 16: Data Types
sc_bigint<length>, sc_biguint<length>
  Used when more than 64 bits of precision are required
  Not optimal for bit vector manipulation
  A two's-complement representation is used for signed integers
  An array of bits
      Can address an individual bit
      Interpreted as an integer for arithmetic operations

## Slide 17: Data Types
sc_int<5> a; // a is a 5-bit signed integer
sc_uint<44> b; // b is a 44-bit unsigned integer
sc_int<3> c;
sc_bigint<5> a;
a = 13; // a gets 01101, a[4] = 0, a[3] = 1, …, a[0] = 1
bool b;
b = a[4]; // b gets 0
b = a[3]; // b gets 1
sc_bigint<3> c;
c = a.range(3, 1); // c gets 110 - interpreted as -2
sc_int, sc_uint, sc_bigint, sc_biguint syntax:

## Slide 18: Data Types
sc_logic
  Interpreted as a single-bit variable representing multiple-valued logic
  Values:
    0 logical zero or false (equivalent to bool false)
    1 logical one or true (equivalent to bool true)
    Z high impedance
    X unknown
  Use only when necessary to model tri-state buses and their drivers.
  Simulation & Synthesis interpret “X” differently; Simulation - unknown, Synthesis - don’t care
  Try to limit assignments of X to internal variables, not the output nodes of your module.

## Slide 19: Data Types
sc_logic syntax:
Syntax:
  sc_logic variable_name, variable_name, … ;
Example:
sc_logic a, b; // declares variables ‘a’ and ‘b’ as type sc_logic
This is a model of a Tri-state driver.
{
bool control, data;
sc_logic ts_out;
if (control == false) {
  ts_out = ’Z’; // Set the drive to Z
}
else {
  ts_out = data; // Set the drive to data
}
}

## Slide 20: Data Types
sc_bit
  Interpreted as a single-bit variable representing two-valued logic
  Values:
    0 logical zero or false (equivalent to bool false)
    1 logical one or true (equivalent to bool true)
Syntax:
  sc_bit variable_name, variable_name, … ;
Example:
sc_bit a, b; // declares variables ‘a’ and ‘b’ as type sc_bit

## Slide 21: Notion of Time
SystemC provides the sc_time data type to measure time
Time is expressed in two parts:
  Numeric magnitude
  Time unit
SC_SEC // seconds
SC_MS // milliseconds
SC_US // microseconds
SC_NS // nanoseconds
SC_PS // picoseconds
SC_FS // femtoseconds
sc_time name...; // no initialization
sc_time name (magnitude, timeunits)...;

## Slide 22: Notion of Time
SystemC allows addition, subtraction, scaling, and other related operations on sc_time objects.
SC_ZERO_TIME is special constant, which is simply sc_time(0, SC_SEC)
sc_time t_PERIOD(5, SC_NS) ;
sc_time t_TIMEOUT (100, SC_MS) ;
sc_time t_MEASURE, t_CURRENT, t_LAST_CLOCK;
t_MEASURE = (t_CURRENT-t_LAST_CLOCK) ;
if (t_MEASURE > t_HOLD) { error ("Setup violated") }

## Slide 23: Notion of Time
sc_start() is a key method in SystemC, it starts the simulation phase
sc_start() takes an optional argument of type sc_time, which determines the maximum simulation time
sc_start(); //sim "forever"
sc_start (max_sc_time); //sim no more than max_sc_time

## Slide 24: Notion of Time
sc_time_stamp() returns current time
wait(sc_time) delays a process for specified time interval
sc_simulation_time() returns simulation time in default time units
sc_set_default_time_unit() establishes default time unit
sc_set_time_resolution() specifies time resolution
void simple_process_ex::my_thread_process (void) {
wait (10,SC_NS);
std::cout<< "Now at "<< sc_time_stamp() << std::endl;
sc_time t_DELAY(2,SC_MS); // keyboard debounce time
t_DELAY *= 2;
std::cout<< "Delaying "<< t_DELAY<< std::endl;
wait(t_DELAY);
std::cout << "Now at " << sc_time_stamp()
<< std::endl;
}

## Slide 25: Notion of Time
int sc_main(int argc, char* argv[]) {// args unused
  sc_set_time_resolution ( 1 ,SC_MS);
  sc_set_default_time_unit(1,SC_SEC);
  simple_process_ex my_instance("my_instance");
  sc_start(7200,SC_SEC); // Limit simulation to 2
  // hours
  double t = sc_simulation_time();
  unsigned hours = int(t / 3600.0);
  t -= 3600.0*hours;
  unsigned minutes = int(t / 60.0);
  t -= 60.0*minutes;
  double seconds = t;
  cout<< hours<< " hours "
  << minutes<< " minutes "
  << seconds<< " seconds" //to the nearest ms
  << endl;
  return 0 ;
}

## Slide 26: Modules
A SystemC module is the smallest container of functionality with state, behavior and structure for hierarchical connectivity
A SystemC module is simply a C++ class
SC_MODULE macro is used to declare the class
#include <systemc.h>
SC_MODULE(module_name) {
MODULE_BODY
};
#define SC_MODULE (module_name) \
struct module_name: public sc_module

## Slide 27: Modules
Module body:
  Ports
  Member channel instances
  Member data instances
  Member module instances (sub-designs)
  Constructor
  Destructor
  Process member functions (processes)
  Helper functions

## Slide 28: Modules
The SC_MODULE constructor performs several tasks specific to SystemC:
  Initializing/allocating sub-designs
  Connecting sub-designs
  Registering processes with SystemC kernel
  Providing static sensitivity
  Miscellaneous user-defined setup
SC_CTOR(module_name)
: Initialization // OPTIONAL
{
Subdesign_Allocation
Subdesign_Connectivity
Process_Registration
Miscellaneous_Setup
}

## Slide 29: Process
A SystemC process is a member function or class method of an SC_MODULE that is invoked by the scheduler in the SystemC simulation kernel.
Process types:
  SC_THREAD
  SC_METHOD
  SC_CTHREAD
Example:
//FILE: simple_process_ex.h
SC_MODULE(simple_process_ex) {
SC_CTOR(simple_process_ex) {
SC_THREAD(my_thread_process);
}
void my_thread_process(void);
};

## Slide 30: Process
Process describes functionality
Processes communicate with each other through signals and channels
Processes can be combined into modules to create hierarchy
Process 1
Process 3
Process 2
Process 5
Process 4
Module 1
signals
System
channel

## Slide 31: Module Hierarchy
sc_main
car_i
eng_i
body_i
fuelmix_i
cyl_i1
exhaust_i
cyl_i2
wheel_FL
wheel_FR
Car
Engine
FuelMix
Cylinder
Exhaust
Body
Wheel
SC_MODULE’s

## Slide 32: Events
A SystemC event is the occurrence of an sc_event notification and happens at a single point in time. An event has no duration or value.
SystemC simulation kernel is an event-driven simulator
Processes wait for an event by using static or dynamic sensitivity
Only two actions can be performed with an sc_event:
  Wait for an event
  Cause event to occur

## Slide 33: Simplifed SystemC Simulation Engine
Elaborate
Cleanup
sc_start()
sc_main()
Initialize
Evaluate
Advance
Time
SystemC Simulation Kernel
Execute code possibly issuing events or updates. Either suspend waiting or exit entirely.
.notify()
immediate
.notify(t)
timed
.notify(SC_ZERO_TIME)
delayed
While processes Ready

## Slide 34: Processes and Event Pools
P1
P2
P3
P4
P5
P6
E1@0
E2@t1
E3@t1
E4@t2
Ready
Running
Waiting
Events
done

## Slide 35: Waiting for Events
SC_THREAD processes are started once and only once by the simulator
Two ways of passing control back to the simulator:
  Exit (return method)
  Suspend (wait method) – dynamic sensitivity
wait(time);
wait(event);
wait(event1 | eventn…) // any of these
wait(event1 & eventn…) // all of these
wait(timeout, event); // event with timeout
wait ( timeout, event1 | eventn…) //any event with
// timeout
wait ( timeout, event1 & eventn…) //all events with
// timeout
wait(); // static sensitivity

## Slide 36: Triggering Events
Events occur explicitly by using notify() method
Invoking an immediate notify() causes any process waiting for the event to be immediately moved from the wait pool into the ready pool for execution
Delayed notifications occur when a time of zero is specified
Timed events are scheduled to occur at some time in the future
sc_event may have no more than a single outstanding scheduled event
Scheduled events may be canceled with the cancel() method
// Object–oriented style (preferred)
event_name.notify(); //immediate notification
event_name.notify(SC_ZERO_TIME) ; // delayed notification
event_name.notify(time); //timed notification
// Functional–call style
notify(event_name); //immediate notification
notify(event_name, SC_ZERO_TIME) ; // delayed notification
notify(event_name, time); //timed notification

## Slide 37: SC_METHOD
SC_METHOD processes are not allowed to suspend
SC_METHOD processes run completely and return
The simulation engine calls them repeatedly based on the dynamic or static sensitivity
SC_METHOD processes dynamically specify their sensitivity by means of the next_trigger() method
The next_trigger method has the effect of temporarily setting a sensitivity list that affects the SC_METHOD
next_trigger(time);
next_trigger(event);
next_trigger(event1 | eventi..); //any of theses
next_trigger(event1 & eventi..); //all of theses required
next_trigger(timeout, event); //event with timeout
next_trigger(timeout, event1 | eventi..); //any + timeout
next_trigger(timeout, event1 & eventi..);//all + timeout
next_trigger(); //re-establish static sensitivity

## Slide 38: Static Sensitivity
Static sensitivity establishes the parameters for resuming during elaboration (i.e. before simulation begins)
Once established, sensitivity parameters can not be changed
Static sensitivity is established:
  with a call to the sensitive() method
  using the overloaded stream operator<<
Syntax:
// IMPORTANT: Must follow process registration
sensitive << event [<< event] ;// streaming style
sensitive (event [, event] ); // functional style

## Slide 39: Channels
Channels encapsulate complex communications
A SystemC channel is a class that implements one or more SystemC interface classes and inherits from either sc_channel or sc_prim_channel. A channel implements all the methods of the inherited interface classes.
Two types:
  Primitive
  Hierarchical

## Slide 40: Primitive Channels
Primitive channels contain no hierarchy, no processes, and are designed to be very fast due to their simplicity
All primitive channels inherit from the base class sc_prim_channel
sc_mutex
sc_semaphore
sc_fifo

## Slide 41: sc_mutex
Any process that needs the shared resource must lock the mutex to prevent other processes from using the shared resource
The process should unlock the mutex when the resource is no longer needed
sc_mutex NAME;
// To lock the mutex NAME (wait until
// unlocked if in use)
NAME.lock();
// Non-blocking, returns true if success, else false
NAME.try lock()
// To free a previously locked mutex
NAME.unlock();

## Slide 42: sc_semaphore
Used for resources, for which you can have more than one copy or owner
sc_semaphore NAME(COUNT);
//To lock a mutex, NAME (wait until
// unlocked if in use)
NAME.wait();
// Non-blocking, returns true if success else false
NAME.trywait()
//Returns number of available semaphores
NAME.get_value()
//To free a previously locked mutex
NAME.post();

## Slide 43: sc_fifo
First-in first-out queues (i.e. FIFOs) are a common data structure used to manage data flow
sc_fifo<ELEMENT_TYPENAME> NAME(SIZE);
NAME.write (VALUE);
NAME.read (REFERENCE) ;
… = NAME.read () /* function style */
if (NAME.nb_read (REFERENCE)) { // Non-blocking
// true if success
…
}
if (NAME.num_available() == 0)
wait(NAME.data_written_event());
if (NAME.num_free() == 0)
next_trigger(NAME.data_read_event());

## Slide 44: Evaluate-update problem
How to model shift register?
D
Q
D
Q
D
Q
D
Q
DATA
SYNC
reg1
reg2
reg3
reg4
Q1
Q2
Q3
Q4

## Slide 45: Full SystemC Simulation Engine
Elaborate
Cleanup
sc_start()
sc_main()
Initialize
Evaluate
Advance
Time
SystemC Simulation Kernel
Execute code possibly issuing events or updates. Either suspend waiting or exit entirely.
.notify()
immediate
.notify(t)
timed
.notify(SC_ZERO_TIME) delayed
While processes Ready
Update

## Slide 46: Evaluate-Update Channels
Special channels, known as signal channels use update phase as a point of data synchronization
To accomplish this synchronization, every channel has two storage locations:
  Current value
  New value
Process calls request_update() to cause the simulation kernel to call the channel’s update() method during the update phase
s1 = v2
s2 = v3
v0
v1
New
Current
s1
s2
update()

## Slide 47: Evaluate-Update Channels
sc_signal, sc_buffer
  sc_signal and sc_buffer use the evaluate-update paradigm
  sc_signal<> is identical to VHDL’s signal
sc_signal<datatype> signame[, signamei]...;
signame.write(newvalue);
signame.read(varname);
sensitive << signame.default_event();
wait(signame.default_event()|...);
if (signame.event() == true) {
// occurred in previous delta-cycle

## Slide 48: Evaluate-Update Channels
sc_signal_resolved, sc_signal_rv
  Non-resolved signals may have only one writer
  Resolved signals may have multiple writers (drivers)
X
0
1
Z
X
X
X
X
X
0
X
0
X
X
1
1
Resolve
X
0
1
Z
X
0
1
Z
EC
SA
SB
SC
EA
EB
BUS
SR
sc_signal_resolved name;
sc_signal_rv<WIDTH> name;

## Slide 49: Evaluate-Update Channels
The specialized templates sc_signal<bool> and sc_signal<sc_logic> have following extensions:
sensitive << signame.posedge_event()
<< signame.negedge_event();
wait(signame.posedge_event() | signame.negedge_event());
if (signame.posedge_event()
|signame.negedge_event()) {

## Slide 50: Ports
Ports of a module are external interface that pass information to and from a module, and trigger actions within the modules
Channels create connections between module ports allowing modules to communicate.
Ports are always defined within the module class definition
sc_port<interface> portname;
SC_MODULE(stereo_amp) {
sc_port<sc_fifo_in_if<int> > soundin_p;
sc_port<sc_fifo_out_if<int> > soundout_p;
…
};

## Slide 51: Ports
Power of interfaces:
  With no change to the definition of modA and modB, we can swap out FIFO for a different channel
modA
modA
sc_fifo<T>
modB
modC
modB
Big_bus_chan
sc_fifo_out_if<T>
sc_fifo_in_if<T>

## Slide 52: Port Connection Mechanics
Modules are connected to channels after both the modules and channels have been instantiated
Two syntaxes for connecting ports:
  By name
  By position
mod_inst.portname(channel_instance); // Named
mod_instance(channel_instance,...); // Positional

## Slide 53: Port Connections

## Slide 54: Accessing Ports
sc_port overloads the C++ operator->(), which allows simple syntax to access the referenced interface
portname->method(optional_args);
…
sc_port<sc_fifo_in_if<int> > soundin_p;
sc_port<sc_fifo_out_if<int> > soundout_p;
…
soundin_p->read();
…
soundout_p->write(ERROR);

## Slide 55: Ports – Standard Interfaces
sc_fifo<> interfaces:
  sc_fifo_in_if<>
  sc_fifo_out_if<>
// Definition of sc_fifo<T> input interface
template <class T>
struct sc_fifo_in_if : virtual public sc_interface {
  virtual void read( T& ) = 0;
  virtual T read() = 0;
  virtual bool nb_read( T& ) = 0;
  virtual int num_available() const = 0;
  virtual const sc_event&
  data_written_event() const = 0;
};
// Definition of sc_fifo<T> output interface
template <class T>
struct sc_fifo_out_if: virtual public sc_interface {
  virtual void write (const T& ) = 0;
  virtual bool nb_write (const T& ) = 0;
  virtual int num_free()const = 0;
  virtual const sc_event&
  data_read_event() const = 0;
};

## Slide 56: Ports – Standard Interfaces
sc_signal<> interfaces:
  sc_signal_in_if<>
  sc_signal_out_if<> (synonym of sc_signal_inout_if<>)
// Definition of sc_signal<T> input interface
template <class T>
struct sc_signal_in_if : virtual public sc_interface {
  virtual const sc_event&
  value_changed_event() const = 0;
  virtual const T& read() const = 0;
  virtual const T& get_data_ref() const = 0;
  virtual bool event () const = 0;
};
// Definition of sc_signal<T> input/output interface
template <class T>
struct sc_signal_inout_if: public sc_signal_in_if<T>
{
virtual void write ( const T& ) = 0;
};
#define sc_signal_out_if sc_signal_inout_if

## Slide 57: Simple Pipeline
Simulation of a simple 3 stage pipelined arithmetic operation
stage1.h, stage2.h, stage3.h contain processes declarations
stage1.cpp, stage2.cpp, stage3.cpp contain processes functionality
numgen.h and display.h contain the stimulus and control process declarations
numgen.cpp and display.cpp contain the stimulus and control functionality
main.cpp contains main entry point and instantiates all processes
main.cpp
stage1.cpp
stage1.h
stage2.cpp
stage2.h
stage3.cpp
stage3.h

## Slide 58: Simple Pipeline
Stage1
Stage2
Stage3
a
a
a
b
b
b
a+b
a-b
a*b
a/b
a^b
in1
in2
sum
diff
prod
quot
powr
<double>
<double>
<double>
<double>
<double>
<double>
<double>

## Slide 59: Simple Pipeline – Stage 1
#ifndef STAGE1_H
#define STAGE1_H
struct stage1 : sc_module {
sc_in<double> in1; //input 1
sc_in<double> in2; //input 2
sc_out<double> sum; //output 1
sc_out<double> diff; //output 2
sc_in<bool> clk; //clock
void addsub(); //method implementing functionality
//Counstructor
SC_CTOR( stage1 ) {
SC_METHOD( addsub ); //Declare addsub as SC_METHOD and
dont_initialize();
sensitive_pos << clk; //make it sensitive to positive clock edge
}
};
#endif

## Slide 60: Simple Pipeline – Stage 1
#include "systemc.h"
#include "stage1.h"
//Definition of addsub method
void stage1::addsub()
{
double a;
double b;
a = in1.read();
b = in2.read();
sum.write(a+b);
diff.write(a-b);
} // end of addsub method

## Slide 61: Simple Pipeline – Stage 2
#ifndef STAGE2_H
#define STAGE2_H
struct stage2 : sc_module {
sc_in<double> sum; //input port 1
sc_in<double> diff; //input port 2
sc_out<double> prod; //output port 1
sc_out<double> quot; //output port 2
sc_in<bool> clk; //clock
void multdiv(); //method providing functionality
//Constructor
SC_CTOR( stage2 ) {
SC_METHOD( multdiv ); //Declare multdiv as SC_METHOD and
dont_initialize();
sensitive_pos << clk; //make it sensitive to positive clock edge.
}
};
#endif

## Slide 62: Simple Pipeline – Stage 2
#include "systemc.h"
#include "stage2.h"
//definition of multdiv method
void stage2::multdiv()
{
double a;
double b;
a = sum.read();
b = diff.read();
if( b == 0 )
b = 5.0;
prod.write(a*b);
quot.write(a/b);
} // end of multdiv

## Slide 63: Simple Pipeline – Stage 3
#ifndef STAGE3_H
#define STAGE3_H
struct stage3: sc_module {
sc_in<double> prod; //input port 1
sc_in<double> quot; //input port 2
sc_out<double> powr; //output port 1
sc_in<bool> clk; //clock
void power(); //method implementing functionality
//Constructor
SC_CTOR( stage3 ){
SC_METHOD( power ); //declare power as SC_METHOD and
dont_initialize();
sensitive_pos << clk; //make it sensitive to positive clock edge
}
};
#endif

## Slide 64: Simple Pipeline – Stage 3
#include <math.h>
#include "systemc.h"
#include "stage3.h"
//Definition of power method
void stage3::power()
{
double a;
double b;
double c;
a = prod.read();
b = quot.read();
c = (a>0 && b>0)? pow(a, b) : 0.;
powr.write(c);
} // end of power method
#endif

## Slide 65: Simple Pipeline – Numgen
#ifndef NUMGEN_H
#define NUMGEN_H
struct numgen : sc_module {
sc_out<double> out1; //output 1
sc_out<double> out2; //output 2
sc_in<bool> clk; //clock
// method to write values to the output ports
void generate();
//Constructor
SC_CTOR( numgen ) {
SC_METHOD( generate ); //Declare generate as SC_METHOD and
dont_initialize();
sensitive_pos << clk; //make it sensitive to positive clock edge
}
};
#endif

## Slide 66: Simple Pipeline – Numgen
#include "systemc.h"
#include "numgen.h"
// definition of the `generate' method
void numgen::generate()
{
static double a = 134.56;
static double b = 98.24;
a -= 1.5;
b -= 2.8;
out1.write(a);
out2.write(b);
} // end of `generate' method

## Slide 67: Simple Pipeline – Display
#ifndef DISPLAY_H
#define DISPLAY_H
struct display : sc_module {
sc_in<double> in; // input port 1
sc_in<bool> clk; // clock
void print_result(); // method to display input port values
//Constructor
SC_CTOR( display ) {
SC_METHOD( print_result ); // declare print_result as SC_METHOD and
dont_initialize();
sensitive_pos << clk; // make it sensitive to positive clock edge
}
};
#endif

## Slide 68: Simple Pipeline – Numgen
#include "systemc.h"
#include "display.h"
#include <stdio.h>
//Definition of print_result method
void display::print_result()
{
printf("Result = %f\n", in.read());
} // end of print method

## Slide 69: Simple Pipeline – Main
#include "systemc.h"
#include "stage1.h"
#include "stage2.h"
#include "stage3.h"
#include "display.h"
#include "numgen.h"
#define NS * 1e-9
int sc_main(int ac, char *av[])
{
//Signals
sc_signal<double> in1;
sc_signal<double> in2;
sc_signal<double> sum;
sc_signal<double> diff;
sc_signal<double> prod;
sc_signal<double> quot;
sc_signal<double> powr;
//Clock
sc_signal<bool> clk;

## Slide 70: Simple Pipeline – Main
numgen N("numgen"); //instance of `numgen' module
N(in1, in2, clk ); //Positional port binding
stage1 S1("stage1"); //instance of `stage1' module
//Named port binding
S1.in1(in1);
S1.in2(in2);
S1.sum(sum);
S1.diff(diff);
S1.clk(clk);
stage2 S2("stage2"); //instance of `stage2' module
S2(sum, diff, prod, quot, clk ); //Positional port binding
stage3 S3("stage3"); //instance of `stage3' module
S3( prod, quot, powr, clk); //Positional port binding
display D("display"); //instance of `display' module
D(powr, clk); //Positional port binding

## Slide 71: Simple Pipeline – Main
sc_start(0); //Initialize simulation
for(int i = 0; i < 50; i++){
clk.write(1);
sc_start( 10 NS );
clk.write(0);
sc_start( 10 NS );
}
return 0;
}

## Slide 72: Simple Pipeline – Output
Result = 0.000000
Result = 0.000000
Result = 0.000000
Result = 0.000000
Result = 788066329449454916075520.000000
Result = 50253081564618617257984.000000
Result = 3785504588212786429952.000000
Result = 331876704603786051584.000000
Result = 33420444988898119680.000000
Result = 3820952118187877888.000000
Result = 490858804069859968.000000
Result = 70202627078491096.000000
Result = 11085844451580030.000000
Result = 1918564708588393.250000
…
Result = 1137.197387
Result = 642.367483
Result = 369.596546
Result = 216.488204
Result = 129.031386
Result = 78.222784
Result = 48.217197
Result = 30.212864
Result = 19.241416

## Slide 73: OSCI Members
Corporate members:
  ARM Ltd.
  Cadence Design Systems, Inc.
  CoWare, Inc.
  Forte Design Systems
  Mentor Graphics Corporation
  Royal Philips Electronics
  STMicroelectronics
  Synopsys, Inc.
Associate corporate members:
  Atrenta, Inc.
  Calypto Design Systems, Inc.
  Carbon Design Systems
  Celoxica Ltd.
  ChipVision Design Systems AG
  ESLX, Inc.
  Fraunhofer Institute for Integrated Circuits
  Intel Corporation
  Jeda Technologies, Inc.
  NEC Electronics America
  Prosilog SA
  SpiraTech Ltd.
  Summit Design, Inc.
  Synfora Inc.
  Tenison EDA

## Slide 74: Conclusion
Executable specifications are potential replacement for the traditional written specifications
Executable specifications are expected to provide unambiguity, completeness and correctness to system specification
SW programming languages like C and C++ are used as a basis for executable specification design environment
SystemC allows design teams to model and verify designs expressed at a true system level of abstraction
Synthesis tools exist and support subset of SystemC constructs
SystemC has its drawbacks and limitations:
  Use of macros is discouraged in C++
  Breaks the distinction between interface definition files and implementation files
  Prevents use of inheritance
SystemC is still evolving and has a lot of potential