## Slide 1: TRIPS Primary Memory System
Simha Sethumadhavan
Email: simha@cs.columbia.edu

## Slide 2: Motivation
Trends
  Wire-delay  partitioned microarchitecture  partitioned memory system
  Memory-wall  large-instruction windows  high-bandwidth memory system
Challenges
  Maintain sequential memory semantics (inherently centralized)
  Low-latency despite communication delays
  High bandwidth despite sequential memory semantics
Solutions
  Distributed LSQ
  Memory-side dependence predictor
  Address-interleaved LSQs, Caches and MSHRs

## Slide 3: TRIPS Architectural Features
Load/Store Ordering (Sequential Semantics)
  Track load/store dependences using LSIDs
  Encoded in a 5-bit field as part of the instruction
TRIPS Block-atomic execution
  Architecture state updated only when all register and memory outputs have been generated
  Block header encodes number of store outputs per block
Weak Consistency

## Slide 4: Major D-Tile Responsibilities
Provide D-cache access for arriving loads and stores
Perform address translation with DTLB
Handle cache misses with MSHRs
Perform dynamic memory disambiguation with load/store queues
Perform dependence prediction for aggressive load/store issue
Detect per-block store completion
Write stores to caches/memory upon commit
Store merging on L1 cache misses

## Slide 5: Load Execution Scenarios
TLB | Dep. Pr | LSQ | Cache | Response
Miss | - | - | - | Report TLB Exception
Hit | Wait (Hit) | - | - | Defer load until all prior stores are received. Non deterministic latency
Hit | Miss | Miss | Hit | Forward data from L1 Cache
Hit | Miss | Miss | Miss | Forward data from L2 Cache (or memory) Issue cache fill request (if cacheable)
Hit | Miss | Hit | Hit | Forward data from LSQ
Hit | Miss | Hit | Miss | Forward data from LSQ Issue cache fill request (if cacheable)

## Slide 6: Load Pipeline
Common case: 2 cycle load hit latency
For LSQ hits, load latency varies between 4 to n+3 cycles, where n is size of the load in bytes
  Stalls all pipelines except forwarding stages (cycles 2 and 3)
TLB Hit
DP Miss
Cache Hit
LSQ Miss
Cycle 1
Access Cache, TLB, DP, and LSQ
Cycle 2
Load Reply
TLB Hit
DP miss
Cache Hit/Miss
LSQ Hit
Cycle 1
Access Cache, TLB, DP, and LSQ
Cycle 2
Identify Store in the LSQ
Cycle 3
Read Store Data
Cycle 4
Load Reply
Stall Pipe
Stall Pipe

## Slide 7: Deferred Load Pipeline
Deferred Load Processing (a.k.a. Replay pipe)
Cycle X+1
Prepare Load for Replay
Cycle X+2
Re-execute
as if new load
Dependence Predictor Hit
Cycle 1
Access Cache, TLB, DP, and LSQ
Cycle 2
Mark Load Waiting
Cycle X
All Prior Stores Arrived
Stall Pipe
Stall Pipe
Deferred loads are woken up when all prior stores have arrived at D-tiles
  Loads between two consecutive stores can be woken up out-of-order
Deferred loads are re-injected into the main pipeline, as if they were new load
  During this phase, loads get the value from dependent loads, if any
Pipeline stall
  When deferred load in cycle X+2 cannot be re-injected into the main pipeline
  Load cannot be prepared in cycle X+1 because of resource conflicts in the LSQ

## Slide 8: Store Commit Pipeline
Stores are committed in LSID and block order at each D-tile
  Written into L1 cache or bypassed on a cache miss
  One store committed per D-tile per cycle
    Up to four stores total can be committed every cycle, possibly out-of-order
  T-morph: Store commits from different threads are not interleaved
On a cache miss, stores are inserted into the merge buffer
Commit pipe stalls when cache ports are busy
  Fills from missed loads take up cache write ports
Store
Commit
Cycle 1
Pick Store
to commit
Cycle 2
Read Store data from LSQ
Cycle 3
Access cache
tags
Cycle 4
Check for hit
or miss
Stall Pipe
Cycle 5
Write to
Cache or
Merge buffer
Stall Pipe

## Slide 9: Store Tracking
Need to share store arrival information between D-tiles
  Block completion
  Waking up deferred loads
Data Status Network (DSN) is used to communicate store arrival information
  Multi-hop broadcast network
  Each link carries store FrameID and store LSID
DSN Operation
  Store arrival initiates transfer on DSN
  All tiles know about the store arrival after 3 cycles
GSN Operation
  Completion can be detected at any D-tile but special processing in done in D-tile0 before sending it to G-tile
  Messages sent on DSN
Store arrival
DT3
CYCLE 0
CYCLE 1
CYCLE 1
CYCLE 2
Block Completion
Signal
DT2
DT1
DT0
Store count
counter
GSN
Inactive DSN
Active DSN

## Slide 10: Load and Store Miss Handling
Load Miss Operation
  Cycle 1: Miss determination
  Cycle 2: MSHR allocation and merging
  Cycle 3: Requests sent out on OCN, if available
Load Miss Return
  Cycle 1: Wake up all loads waiting on incoming data
  Cycle 2: Select one load; data for the load miss starts arriving
  Cycle 3: Prepare load and re-inject into main pipeline, if unblocked
Store Merging
  Attempts to merge consecutive writes to same line
  Snoops on all incoming load misses for coherency
Resources are shared across threads

## Slide 11: D-Tile Pipelines Block Diagram
Coherence checks e.g. Load and store misses to same cache line
CC
Cache
Store Port
arb
Missed load pipeline
Spill Mgmt
Line fill pipeline
Store commit pipeline
Replay load pipeline
Cache + LSQ
Load Port
ST X
LD X
BYPASSES
Unfinished store bypassing to load in previous stage. Bypassing=> fewer stalls => higher throughput
Miss handling
L2 Req.
Channel
arb
arb
Load input from
E-Tile
Load output to
E-Tile
Store miss pipe
Store hit
Costly resources are shared e.g. cache and LSQ ports, L2 bandwidth
To cite: Design and Implementation of the TRIPS Primary Memory System, ICCD 2006
Email: simha@cs.columbia.edu.